## Slide 1: Upgraded Inner Tracking System for ALICE at the LHC: Status and Plans
Grigory Feofilov (on behalf of the ALICE collaboration)
Saint-Petersburg State University
The 3rd International conference on particle physics and astrophysics (ICPPA-2017), Moscow, 2-5 October 2017, MEPhI, Moscow
Acknowledgement: This work was supported for the SPbSU participants in 2016 within the Program of Russian groups activities in the ALICE upgrade by the Ministry of Education and Science of Russian Federation, contract No14.610.21.0003, identification number RFMEFI61014X0003 (SPbSU identification number No. 11.19.1632.2014).
3D view of the new ITS by Corrado Gargiulo

## Slide 2: Outline
Motivation.
Upgrade of ALICE/ITS
  General design
  Detectors and readout
  General layout
  Production status
3) Plans and summary of new physics possibilities

## Slide 3
ALICE installation at the LHC
Central Detectors:
Inner Tracking System
(SPD,SDD,SSD – 6 layers
between 39 and 430 mm)
Time Projection Chamber
Time-of-Flight
Transition Radiation Detector
Spectrometers:
High Momentum PID (RICH)
Photon Multiplicity
Forward Multiplicity
Muon Spectrometer
Calorimeters:
EM Calorimeter
Photon Spectrometer (PHOS)
Zero Degree Calorimeter
Trigger:
Trigger Detectors
pp High-Level-Trigger

## Slide 4: Current ITS performance
Distribution of the energy-loss signal in the ITS
as a function of momentum.
International Journal of Modern Physics A Vol. 29,
No. 24 (2014) 1430044
International Journal of Modern Physics A Vol. 29,
No. 24 (2014) 1430044

## Slide 5: Some physics results of Run-2: D meson elliptic flow puzzle
PRL 111, 102301 (2013)
Elliptic flow for D-mesons?

## Slide 6: Why heavy quarks as one of the main motivations?
Study the early stages
in heavy-ion collisions
Probe to study
thermalization
of Quark Gluon Plasma (QGP)
Microscopic insight into
transport properties of the medium
1] T. Matsui and H. Satz, Phys. Lett. B 178 (1986) 416.
[2] Helmut Satz, Calibrating the In-Medium Behavior of Quarkonia, arXiv: 1303.3493, 12 April 2013
[3] 2013 -- Berndt Müller, arXiv:1309.7616
C
C
__

## Slide 7
Coverage in transverse momentum to be as complete as possible,
in particular down to zero momentum
2. Very accurate identification of secondary vertices
from decaying charm or beauty (D, J/psi, , ).
  Design goals to be met in the upgrade:
CERN-LHCC-2012-013 (LHCC-P-005)
Comparison of ALICE,ATLAS and CMS upgrade
Λc
Λb

## Slide 8
  Identification of secondary vertices
CERN-PH-EP-2012-XXX March 6, 2012
Schematic view of the D0 decay
in the D0 → K−π+ channel.
D0 → K−π+
secondary
vertex position
resolutions vs. pT:
for current and
upgrade scenarios:
x (left) and
z (right)
coordinates.
Impact parameter ~100μm

## Slide 9
Challenges and requirements:
   New, high-resolution, low-material, fully-monolithic inner tracker based on CMOS sensors!
Improve impact parameter resolution factor of ~3 in r-φ (z) at 500 MeV/c)
First layer closer to interaction point: r0 = 39 mm → 22 mm
Smaller beam pipe radius: 29 mm → 18.2 mm
Smaller pixel size: 50 μm x 425 μm → 28 μm x 28 μm
Improve tracking efficiency and pT resolution at low pT
Increase the number of layers 6 →7
Easier maintenance
Fast readout : 1 kHz → 50 kHz in Pb-Pb, 200 kHz in pp
Low-material budget (< 0.3% Xo for 3 inner layers)
CDR: Endorsed by LHCC
in Sept. 2012 ITS Upgrade TDR:
in March 2014

## Slide 10: Upgraded ALICE ITS design
Based on high resistivity epitaxial layer
Monolithic Active Pixel Sensors (MAPS)

## Slide 11: CMOS Pixel Sensor
Schematic of MAPS pixel
in imaging CMOS TowerJazz 0.18 μm technology
TowerJazz 0.18μm CMOS Imaging Process
Pixel pitch ~ 30 μm
High-resistivity (> 1kΩ cm) p-type
epitaxial layer (25μm) on p-type substrate
Small n-well diode (2 μm diameter),
=> low capacitance
Reverse bias voltage to substrate
(contact from the top) can be used
to increase depletion zone around NWELL collection diode
Deep PWELL shields NWELL of PMOS
Transistors
Very low power dissipation
(<300nW/pixel)
J. Phys. G: Nucl. Part. Phys. 41 (2014) 087002

## Slide 12: PIXEL Chip – General Requirements and ALPIDE Specifications
ALICE-TDR-017, Upgrade of the ALICE Inner Tracking System , CERN-LHCC-2013-024 02 December 2013
Parameter | Inner Barrel (IB) | Outer Barrel (OB)
Notes: (*) Colour code: ALPIDE specifica:ons if different from requirements (**) 10 x radia:on load integrated over approved programme (~ 6 years of opera:on)

## Slide 13
Chip Production – Overview

## Slide 14
ALPIDE Chip

## Slide 15: ALICE technology for IB staves:
JINST 9 P06005(2014)
ALPIDE chip
Material | Thickness (μm) | Xo (cm) | X/Xo (%)
Polyimide cooling pipe wall | 25 μm | 28.41 | 0.003
Carbon fleece | 40 μm | 106.8 | 0.004
Water | 1mm | 35.76 | 0.032
Carbon fiber plate K13D2U | 70 μm | 26.08 | 0.027
Graphite foil | 30μm | 26.56 | 0.011
Thermal greese (glue) | 100μm | 44.37 | 0.023
Si-sensor | 50μm | 9.36 | 0.064
Total (without FPC) |  |  | 0.154
Total |  |  | <0.3
Record level of radiation transparency <0.3% Xo
24.09.17
Thickness of detector components in terms of fraction of radiation length X/Xo -

## Slide 16: Readout of ALPIDE chips
NIMA 824 (2016) 465–469
Sketch of the ALPIDE architecture.
The Inner Barrel stave readout
The Outer Barrel half-stave readout .
ALPIDE pixel cell

## Slide 17
Upgrade of the ALICE Inner Tracking System
   New, high-resolution, low-material, fully-monolithic inner tracker.

## Slide 18: New ITS design

## Slide 19
Hybrid Integrated Circuit (HIC) and Stave Production
5. HIC gripper fixed to the Alignment station
3. Glue spread on the CP
6. HIC alignment
4. HIC gripped by the HIC gripper

## Slide 20
Stave Assembly – Production Sites
Readiness of laboratories:
Infrastructures and tooling
Training on assembly procedures
Training on test procedures
TORINO
NIKHEF
READY
DONE
DONE
FRASCATI
READY
DONE
DONE
READY
TO BE DONE
TO BE DONE
DARESBURY
READY
DONE
TO BE DONE
READY
DONE
TO BE DONE
BERKELEY

## Slide 21: Stave prototypes
Assembly of Stave-0 completed using prototype HICs
Used to validate design and layout for production readiness review; characterisation results reproduced performance measured on single HICs
Assembly of Stave-1 ongoing; first half-stave completed, tests show all 98 chips fully functional

## Slide 22: 3D view of the new ITS layout
ITS IB
Inner Barrel (ITS IB)
Material thickness per detector layer: ~ 0.3% X/X0 )

## Slide 23: Services Layout in the ALICE Cavern

## Slide 24: Services: Interface Cage of New ITS

## Slide 25: Services, Mechanics and Cooling Overview
IN PRODUCTION PHASE
Dry Assembly Test at the end of 2017

## Slide 26: 2017: Spaceframe production status: IB
Light-high thermal conductive
Cold Plate
Stave Precise positioning
end pieces
Positioning
Cooling
Stiffness
Light-stiff mechanical Space Frame
Space Frame
Filament winding
M60J
0.3 m, 1.7gr
Cold Plate
Embedded polyimide pipes Pyre M.L.®
Manual Layup
Amec FGS_003
K13D 2U
fleece
Water leak-less cooling
(-- below atmospheric pressure).
Pipe Burst pressure at 51bar
Total number of structures needed IB Layer 0,1,2: 12+16+20pc = 48pc; spare 120%; total 106 SF
Number of Space Frame produced to date for the ITS Inner Barrel are 170 out of 106 (40*)
* with connectors and fittings
CARBON PARTS PRODUCTION FINISHED
PRR 27 April 2017
Production at
ITS Plenary Meeting, 10 July 2017. Corrado Gargiulo

## Slide 27
2017: OB Spaceframe Production
27
Positioning
Cooling
Stiffness
1.5 m, 40 g
Light - high thermal conductive
Cold Plate
Stave Precise positioning
End Pieces
Light-stiff mechanical Space Frame
Connection between
Space Frame and Cold Plate
1.5m, 21g
Filament deposition
Manual layup
Carbon peek machined part
Carbon paper (FGA)
Carbon fleece
Polyimide pipes
M55j thread
M55j prepreg
OB ML (layer 3,4): 24+30 pc = 54pc; spare 20%; total 65 SF (130 CP)
OB OL (layer 5,6): 42+48 pc = 90pc; 20%spare; total 108 SF (216 CP)
Total number of structures needed:
* with connectors and fittings
-- for the Middle Layers: 82 SF out of 65 (9*), 140 CP out of 130
--for the Outer Layers: 140 SF out of 108 (12*), 230 CPout of 216 (75*)
Production
at
Spaceframe CARBON PARTS PRODUCTION FINISHED
A set of structures is ready for delivery to the integration centers
Number of Space Frames (SF) and
Cold Plates (CP) produced to date

## Slide 28: Inner Barrel (IB) mock-up and prototype
Composite parts production is well advanced

## Slide 29: DETECTOR BARREL Mechanics production status: IB
END WHEEL carbon parts produced to date 3x EW0, 3x EW1, 3x EW2
END WHEEL carbon assembly produced to date 1x EW1, 0.5x EW2
END WHEEL with ruby pads produced to date 0.5x EW2
Total number of structures needed
Nominal=1 EW0, 1 EW1, 1 EW2 + 1 CYSS; spare 120%; total 3 EW0, 3 EW2, 3 EW3, 3 CYSS
END WHEEL carbon parts
END WHEEL (EW) carbon assembly
EW with ruby pads
CYSS
Cylindrical Structural Shell.
PRR 27 Dec 2016
Production
at
ITS Plenary Meeting, 10 July 2017. Corrado Gargiulo
All assembly jig for ruby pads gluing produced
Number of

## Slide 30: DETECTOR BARREL Mechanics production status: OB
n.1 EW3, n.1 EW4, n.1 EW5,n.1 EW 6, n.1 COSS, n1 CYSS
Total number of structures needed
Number of:
END WHEEL (EW) carbon parts and
END WHEEL with ruby pads produced to date # end production foreseen
EW6 Jul, EW 4 Sept, EW3 5 October 2017
n. of COSS produced to date # end production foreseen Sept
END WHEEL with ruby pads
CYSS
Prototype phase completed, tender closed, contract assigned LOSON, Carbon Material procured, Moulds produced
END WHEEL carbon parts
COSS
Conical Structural Shells
Cylindrical Structural Shells (CYSS) produced to date # end production
was foreseen in July 2017 Conical Structural Shells (COSS)
Prototype phase completed, Carbon Material procured, use of existing mould
PRR 27 Dec 2016
Production at
Loson Compositi
Production at
ITS Plenary Meeting, 10 July 2017. Corrado Gargiulo
Cylindrical Structural Shells

## Slide 31: Service Barrel Mechanics production status: IB and OB
Total number of structures needed: 1 IB Service Barrel, 1 OB Service Barrel
OB SERVICE BARREL production in progress
OB Service Barrel
Prototype phase completed, Carbon Material procured, Mould material procured, Mould machining done in May 2017.
IB SERVICE BARREL production in progress
PRR 5 May 2016
Production at CERN EP DT Composite Lab
Production at
Prototype phase completed, Carbon Material procured, Mould production next
IB Service Barrel

## Slide 32: Outer Barrel Mechanics at LBNL
Fabrication of large composite structures is progressing well, expected to be completed by October 2017
Will be shipped to CERN
Dry assembly test will take place in Nov-Dec 2017

## Slide 33: Service Barrel Patch Panels (PP)
PP layout under study
Power connectors OB-ML (D=22mm), OB-OL 106(D=37 mm)
Increase of connector size (D=24mm),(D=40mm) under study
Final assessment needs definition of Samtec Connector
4- Samtec cables
cooling
The room available at the end of the OB service barrel is limited compared to the number of services and connectors
The patch panel needs to be displaced away from the end of the SB in order
to gain more room for the connectors. Samtec connectors to be decided.
Patch Panel (PP) at OB Service Barrel(SB)

## Slide 34
Production readiness reviews(PRRs)
Sensor Series Production
Stave Develop
2016
2017
2018
2019
2020
Commissioning at Surface
Installation
Commissioning in ALICE
Stave Mechanics
HIC Production
CMOS processing, thinning & dicing, test
Hic and Stave
Stave Production
Mechanical Support Structures
Design & Prototyping
Design & Prototyping
Production & Test
PRR
PRR
Global Assembly
EDR
PRR
Development
Production
2016
2017
2018
2019
2020
EDR
PRR
Readout Electronics
Commiss.
10 months
Dry Assembly Test
Development

## Slide 35: Summary
The following results were provided by the ITS/ALICE collaboration for the upgrade preparation during the LS1:
the Research and Design was completed in 2012–2014;
the evaluation of technologies and prototypes, selection of technologies, engineering, design, TDR, final design - were finished in 2014 -- 2016 .
2017 – Production phase started to provide:
The extremely low material budget for the ITS (~ 0.3% Xo for 3 innermost layers).
Improvement of the impact parameter resolution by a factor of ~3;
Reconstruction of charged particles starting from a pT of ~50 MeV/c, and measurements of charm and beauty mesons down to zero pT ;
Increase of the rate of data taking in Pb–Pb collisions from 1 kHz to ~50 kHz.
The project is well on track to meet the very challenging and ambitious schedule of 2018-2019!
New physics studies in Pb-Pb at the LHC will be opened by ALICE after 2020!

## Slide 36
Technical Design Report for the Upgrade of the ALICE Inner Tracking System
J. Phys. G: Nucl. Part. Phys. 41 (2014) 087002
New physics by ALICE at the LHC
With Pb beams of high luminosity L=7x1027cm-2s-1
Thermalization of partons in the QGP, with focus on the massive charm and beauty quarks.
In-medium parton energy loss mechanism
Quarkonium dissociation as a probe of deconfinement
Production of thermal photons and low-mass dileptons
Production of D mesons, including Ds, down to zero pT will be accessible for the first time.
    Charm and beauty baryons and . .
    For the first time via the decay  Λc + X .
    Baryon/meson ratios for charm ( /D) and for beauty (Λb/B), will be accessible for the first time.
    The elliptic flow (v2) of charmed and beauty mesons and baryons down to low pT will also be accessible for the first time.
    Measurement of beauty via displaced D0  Kp which will be accessible for the first time.
    Measurement of beauty via displaced J/psi  ee, which will also be accessible for the first time.
Gain a factor of 100 in statistics
over original programme
(Run1 + Run2)
Λc
Λb
Λb
Λc

## Slide 37: Back-up slides

## Slide 38
Chip Production – Overview

## Slide 39: ITS Collaboration
Czech Republic (Prague), Slovakia (Kosice),