## Slide 1: The PSD supermodule response study at proton beam energies 2-6 GeV at CERN test beams
Moscow, 2017

## Slide 2
CBM@FAIR and MPD@NICA
Forward hadron calorimeters at CBM and MPD
Structure of calorimeters module
Supermodule of the PSD CBM
Facility for module response study at CERN
Preliminary test results
Summary and outlook
Outline

## Slide 3
APPA
CBM
NUSTAR
PANDA
FAIR accelerator complex in Darmstadt
СВМ experiment
CBM uses forward hadron calorimeter (Projectile Spectator Detector – PSD) to measure centrality and the reaction plane orientation.
Hadron calorimeter consists of 44 modules with transverse sizes
20х20см and 160см length.
Total weight - 22 tons.
SIS100 is aimed to accelerate Au nuclei upto 11GeV/nucleon with intensity upto 109 nuclei/sec.

## Slide 4
NICA accelerator complex in Dubna
MPD experiment
2 forward hadron calorimeters (FHCAL) are used in MPD to measure centrality and the reaction plane orientation.
Each of hadron calorimeters consists of 44 modules with transverse sizes 15х15cm and 110cm length.
Energies (c.m.s.) 4-10 GeV.
Beams – from protons to Au nuclei.
Luminosity – to 1027 Au nuclei.

## Slide 5: Hadron calorimeter module structure
60 lead-scintillator tiles
10 longitudinal sections
6 WLS/MPPC
10 MPPC/module
10 readout channels
MPPC& Preamplifires
All modules for the PSD and FHCAL are produced at INR

## Slide 6
PSD supermodule
test on T10 at CERN (September 2017)
Supermodule – array of 3x3 modules.
Total size 600 x 600 x1650 mm3.
Total weight -5000 Kg.
PSD supermodule placed on
movable platform at T10 beam
Tasks:
PSD modules calibration with beam muons;
Study of PSD supermodule response at 2- 6 GeV/c (proton and pions) with Dubna FEE and readout electronics;

## Slide 7
Test of PSD Supermodule on T10 beam at CERN
(6-20 September 2017)
2 quartz cherenkov detectors provided trigger and used
for beam particle
identification (σt ~ 60 psec)
ToF between 2 beam detectors has been measured by
CAEN DT5742 12 bit 5 GS/s
Switched Capacitor ADC

## Slide 8: Scheme of measurements

## Slide 9
Dubna FEE and readout electronics for supermodule PSD
FEE – 9 boards with 10 MPPCs
and amplifiers (Gain – about 10)
Readout: 2 x 64 channel
fast 12bit ADC64s board, 62.5MS/s
(AFI, JINR)
Ethernet
1Gbit
MPPC
Integrator
τ ~ 50ns
τ ~ 1.2μs
Amp
FEE
ADC64
...
ADC1
FPGA
ADC64s
Hamamatsu MPPC:
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~10%.
Gain 105
Recov. time – 10 nsec

## Slide 10
Beam particle identification on T10
Measured T10 beam composition
vs particle momentum
Chart: 
| 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
Protons | 0.14956 | 0.17519 | 0.20172 | 0.23449 | 0.27419 | 0.31658 | 0.36246 | 0.40221 | 0.45026 | 0.49127
Pions | 0.68037 | 0.64206 | 0.6224 | 0.60813 | 0.58233 | 0.56656 | 0.55001 | 0.52105 | 0.47927
Muons | 0.16465 | 0.17336 | 0.16058 | 0.14048 | 0.11821 | 0.097449 | 0.082502 | 0.072947 | 0.066139
Kaons | 0.0039084 | 0.0083164 | 0.013409 | 0.016446 | 0.02229 | 0.019512
P(GeV/c)
Beam composition

## Slide 11
P
π
μ
TOF vs Energy deposition in supermodule
for 6 Gev/c beam
Energy deposition in supermodule, MeV
TOF between beam counters,psec

## Slide 12
π
μ
P
Reconstructed supermodule energy deposition
of pions and protons with momentum 6GeV/c

## Slide 13
Energy deposition profile
for protons and pions in module 5
Protons 6 GeV/c
Pions 6 GeV/c
Mean E dep, MeV
Mean E dep, MeV
Protons 2 GeV/c
Mean E dep, MeV
Pions 2 GeV/c
Mean E dep, MeV
Cell number
Cell number
Cell number
Cell number

## Slide 14
Supermodule energy resolution
and linearity for protons and pions
Energy resolution
● protons
● pions
E kin , GeV
Pion beam energy, GeV
Mean energy deposition
Mean energy deposition
Proton beam energy, GeV

## Slide 15
Summary and outlook
Response of the PSD CBM has been studied at very low hadron energies for the first time.
PSD modules have been calibrated by beam muons.
Energy resolution and linearity of supermodule were measured for low beam energies
Next test of supermodule at proton beam energies upto 10 GeV is planned to perform in November-December 2017.

## Slide 16
Thanks for your attention

## Slide 17: Backup slides

## Slide 18
Muons selection by supermodule
E dep (chan.) for first five sections of module 5
E dep (chan.) for last five sections of module 5
E dep (chan.) for last five sections of module 5
Muons / Pions separation 6 GeV/c beam
Muons 6 GeV/c with beam dump
in T0 beam line
E dep (chan.) for first five sections of module 5

## Slide 19
Muons energy deposition in 10 sections
of module 5 at beam momentum 6GeV/c
cell 1
cell 2
cell 3
cell 4
cell 5
cell 6
cell 7
cell 8
cell 9
cell 10

## Slide 20
Pions, beam 6GeV/c module5
cell 1
cell 2
cell 3
cell 4
cell 5
cell 6
cell 7
cell 8
cell 9
cell 10

## Slide 21
Protons, beam 6GeV/c module5
cell 1
cell 2
cell 3
cell 4
cell 5
cell 6
cell 7
cell 8
cell 9
cell 10

## Slide 22: Определение центральности
PSD
projectile spectators
participants
STS+MVD
b

## Slide 23: Определение классов центральности по множественности треков
5% of events
CBM simulation, Au+Au, 10AGeV,
1.5M events, UrQMD
CBM simulation Au+Au, 10AGeV
1.5M events UrQMD
PSD1

## Slide 24: Определение плоскости реакции

## Slide 25: Сцинтилляционные пластины
Для съема света в обоих детекторах использовались переизлучающие оптоволокна фирмы Kuraray (Япония) типа Y11(200) S-type диаметром 1 мм.
Пластины для CBM 20х20х0.4 см3 (слева) и MPD 15х15х0.4 см3 (справа)
Спектры поглощения и излучения оптоволокна Y11

## Slide 26: Фотодетектор – микропиксельный лавинный фотодиод
На конце оптоволокна установлен оптический разъем, к которому присоединен микропиксельный лавинный фотодиод.
HAMAMATSU MPPC S12572-010P
Светочувствительная зона | 3 × 3 mm
Шаг пикселя | 10 μm
Количество пикселей | 90000
Спектральная чувствительность | от 320 до 900 nm
Пик чувствительности | 470 nm
Dark count (typ.) | 1000 kcps
Усиление | 1.35×105
Эффективность регистрации фотонов | 10 %