## Slide 1: Thermosyphon cryogenic system for RED-100 detector
International conference on particle physics and astrophysics
National Research Nuclear University MEPhI
5-10 October 2015
A. V. Shakirov (MEPhI)
Moscow

## Slide 2: The challenges for the cryostatting system
Thermosyphon cryogenic system for RED-100 detector
2/9
07.10.2015
1. The detector should be placed inside a massive shield for providing low-background experiment
2. System should provide condensing of 200 kg of xenon and maintaining a stable temperature of the liquid with an accuracy of about 1K in the range of 160-170K during long time required for the experiment
The goal is to develop a powerful cryostatting system with most of the mass located at a distance and with the possibility of precise temperature control
The thermosyphon technology meets the requirements

## Slide 3: The principle of thermosyphon operation
A thermosyphon or a gravity-assisted heat pipe consists of three basic sections:
A cooling section (condenser)
A passive adiabatic section connecting the two active sections
A heating section (evaporator)
A two-phase closed tubular thermosyphon is a device developed for transfer the large heat energies
A heat exchange takes place along heat pipe by condensation and evaporation of N2 in the top and bottom parts of pipe
The gravity division of the working substance in liquid and gaseous states is possible.
Thermosyphon cryogenic system for RED-100 detector
3/9
07.10.2015

## Slide 4: The cryostatting system
Thermosyphon cryogenic system for RED-100 detector
4/9
07.10.2015
Titanium cryostat
Dewar with liquid N2
Thermosyphon in metal hose
Control system

## Slide 5: Thermosyphon types and characteristics
Thermosyphon cryogenic system for RED-100 detector
5/9
07.10.2015
Bellow flex hose thermosyphon
Tubular thermosyphon made of copper pipe
Thermosyphon based on copper pipe is more powerful and should be used in experiment
The comparison of the two types of thermosyphon |  | 
 | Copper pipe | Sylphon
Cooling rate | 3 K/min | 1.3 K/min
The heat transfer limit | 100W | 60W

## Slide 6: Thermal stabilizing control system
Thermosyphon cryogenic system for RED-100 detector
6/9
07.10.2015

## Slide 7
Thermosyphon cryogenic system for RED-100 detector
7/9
07.10.2015
Thermal stabilization results

## Slide 8: Summary cooling and stabilization results
Thermosyphon cryogenic system for RED-100 detector
8/9
07.10.2015

## Slide 9
Thermosyphon cryogenic system for RED-100 detector
9/9
07.10.2015
Conclusions
The cryogenic system based on closed two-phase thermosyphon using nitrogen as an active medium was developed
This system provide thermal stabilization of the emission detector based on a liquid xenon at required temperature with an accuracy of 1K .
Such a system may be used in the RED100 detector