## Slide 1: Thunderstorm investigations based on the data obtained by the URAGAN muon hodoscope and Doppler weather radar DMRL-C
Alexandra KACHURa, Yuri PAVLYUKOVb, Anatoly PETRUKHINa, Natalia SEREBRYANNIKb, Victor SHUTENKOa
aNational Research Nuclear University MEPhI (Moscow Engineering Physics Institute), Scientific & Educational Centre NEVOD
bCentral Aerological Observatory
IV international conference on particle physics and astrophysics
Moscow, 22-26 October 2018

## Slide 2: Muon hodoscope URAGAN
provides registration of muons with a high spatial and angular resolution (about 1 cm and 0.8°, respectively) in a wide range of zenith angles (from 0° to 84°)
track parameters are reconstructed in real time and accumulated in a two-dimensional matrix for one minute interval. Such a matrix is a "muon picture" of the upper hemisphere
characteristics reflecting the distortion of the distribution of the muon flux used in this analysis are:
vector of local anisotropy (A) which indicates the average direction of muon arrival recorded by the detector
vector of relative anisotropy (R) which is the difference between the local anisotropy vector in the current time and averaged over a long period anisotropy vector and its projection on the horizontal plane ()

## Slide 3: Doppler weather (meteorological) radar DMRL-C
Displaying distribution of various meteorological data such as precipitation intensity and velocity and direction of movement of cloud systems
a view range of 250 – 300 km
a maximum detection height of about 20 km
a high spatial resolution (0.5 – 1 km)
Detection of dangerous weather phenomena such as thunderstorms

## Slide 4: The research
Muon pictures (muonographs) and meteorological maps obtained every ten minutes by means of two facilities during thunderstorm periods of spring and summer of 2018 (~27 events) are compared with each other
Wavelet analyses of obtained data are performed
Results are illustrated by thunderstorm events occurred in Moscow on July 14, 2018 and August 30, 2018

## Slide 5: 14.07.2018
The thunderstorm was observed at the Domodedovo airport meteorological station at 14:00 (UTC time) and at the VDNKh meteorological station from 14:00 to 17:00

## Slide 6: Meteorological maps
Start 07:20
Peak 12:00
End 19:20
Precipitation is weak
Moderate precipitation
Precipitation is strong
Cumuliform clouds
Rain is weak
Moderate rain
Heavy rain
Thunderstorm 30-70%
Thunderstorm 70-90%
Thunderstorm> 30%

## Slide 7: Comparison (11:30 – 13:10)

## Slide 8: Wavelet analyses of URAGAN data
Isum
A
Rhor

## Slide 9: Wavelet analyses of URAGAN data
Isum
A
Rhor

## Slide 10: Wavelet analysis: Rhor
T60
T90
T180

## Slide 11: Wavelet analysis: Rhor
T60
T90
T180

## Slide 12: 30.08.2018 – 31.08.2018
The thunderstorm was observed at the Domodedovo airport meteorological station from 21:00 30.08 to 05:00 31.08, at the Balchug meteorological station from 21:00 30.08 to 05:00 31.08 and at the VDNKh meteorological station at 23:00 30.08

## Slide 13: Meteorological maps
Start 30.08 05:00
Peak 30.08 23:50
End
31.08 07:00
Precipitation is weak
Moderate precipitation
Precipitation is strong
Cumuliform clouds
Rain is weak
Moderate rain
Heavy rain
Thunderstorm 30-70%
Thunderstorm 70-90%
Thunderstorm> 30%

## Slide 14: Comparison (20:30 – 05:20)

## Slide 15: Wavelet analyses of URAGAN data
Isum
A
Rhor

## Slide 16: Wavelet analysis: Rhor
T60
T90
T120

## Slide 17: Wavelet analysis: Rhor
T60
T90
T120

## Slide 18: Conclusions
Results obtained from the analysis of data provided by MH URAGAN are consistent with DMRL-C data
Characteristics of the muon flux provide a good reaction to the passage of a thunderstorm
Wavelet analysis of different time series shows that before and during the passage of a thunderstorm there are periodic disturbances in the characteristics of the muon flux. Periods of those disturbances are ranging from 60 to 180 minutes

## Slide 19: Thank you for your attention!

## Slide 20: Characteristics reflecting the distortion of the distribution of the muon flux
Vector of local anisotropy (A) indicates the average direction of muon arrival recorded by the detector. This value is calculated as the sum of unit vectors, each of which has a reconstructed direction of a single muon track, normalized by the total number of muons.
The vector of relative anisotropy (r) is the difference between the local anisotropy vector in the current time and averaged over a long period anisotropy vector
In this analysis, the value of the vector r module and its projection on the horizontal plane (), the projections onto the horizontal axis South () and East (), as well as the projection on the vertical axis () are used
Registration of muon flux variations at the Earth’s surface from different directions allows to obtain a picture of the conditions in the upper atmosphere, to trace the dynamics of their changes and to identify disturbed regions

## Slide 21: 14.07 Wavelet analysis: Isum
T60
T80
T180

## Slide 22: 14.07 Wavelet analysis: A
T60
T90
T120

## Slide 23: 30.08 Wavelet analysis: Isum
T60
T90
T120

## Slide 24: 30.08 Wavelet analysis: A
T80
T120
T160

## Slide 25: Muon diagnostics
The greater the pressure, the
greater muons absorption (due to an increase the amount of substance)
The higher the temperature, the:
higher pion generation point
longer geometric path of the muon to the surface of the Earth
higher probability of decay
Formation of the muon flux: in the atmosphere at an altitude of 10 - 20 km
The top of a typical thunderstorm cell: at a height of 8 - 12 km
The muon flux is modulated by changes in the basic thermodynamic parameters of the atmosphere.

## Slide 26: Wavelet analyses of URAGAN data