## Slide 1
N. Barlykov, V. Dudin, T. Enik, A. Ivanov,
*E. Kokoulina, A. Kutov, E. Martovitski, V. Nikitin,
V. Popov, R. Shuliakovsky
JINR, Russia, *P.O. Sukhoy GSTU, Belarus
6th International Conference on Particle Physics and Astrophysics 29.11.2022-02.12.2022
MiniSPD test bench for testing
of SPD detectors prototypes
On behalf of the SPD Collaboration

## Slide 2
Start of construction: 2013.
Our accelerator complex is being created at the JINR, LHEP (Dubna, RF).
The main aims are the study of:
the properties of dense baryonic matter, a special state of matter in the first moments after the Big Bang, formation of quark-gluon plasma (MPD);
spin structure of proton (deuteron) (SPD).
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia
2
NICA (Nuclotron based Ion Collider fAcility)

## Slide 3
NICA aerial view, April 2022
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 4
BM@N setup
Clean Room
SPD
Detector
MPD
Detector
Collider
Electronic
cooling
Plant of Magnets
Cryogenic system
Nuclotron
Booster
injection complex
NICA scheme
3

## Slide 5
4
The main tasks of SPD project
Spin is one of the fundamental properties of elementary particles. It cannot be explained by a static view of the proton:
total spin = s(q) + s(g) + angular momentum = 1/2.
It’s not just the number 1/2. It is the result of interaction between quarks and gluons, more probably gluons.
The origin of spin is a fundamental problem of physics. Our SPD (Spin Physics Detector) project is aimed at study spin properties of nucleons and light nuclei.
How are quarks and gluons, their spins distributed in space and on momentum inside the nucleon?
2102.00442[hep-ex]Conceptual design of the Spin Physics Detector (A. Guskov)
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 6
5
Direct photons
Nucleon PDFs by J/ψ production
Open charm production: D0, 0, D+/-, C, …
Spin-dependent effects in elastic pp, pd and dd scattering
Spin effects in exclusive hadron production
Spin effects in production of hadrons with high pT
pp, dd, pd polarized beams with energy = 3.4 – 10 GeV
luminosity pp (dd) is estimated up to 1032 (1031) cm-2s-1
The main tasks of SPD project
[SPD Collab. Phys.Part.Nucl. 52 (2021) 6]
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 7
6
Why do we need MiniSPD?
MiniSPD is a setup for testing SPD detector prototypes with cosmic muons
MiniSPD is used to test the Data Acquisition System (DAQ) of SPD
MiniSPD is used to test the Detector Control System (DCS) of SPD
MiniSPD is used to teach students how to work with real detectors
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 8
7
MiniSPD stand for testing SPD’s elements
Trigger subsystem consists of 2
scintillators.
Top: ScintPos[1] = 3 mm.
Bottom: ScintPos[2] =
931,5 mm.
Top
scintillator
Bottom scintillator
Si
Si
Si
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 9
Description of Si-modules
1
2
3
4
6
5
7
8
1 - U/X, 2 – U/X
3 – X/U, 4 – Y/U
5 – U/X, 6 – X/U
7 - U/X, 8 – X/U
Coordinates (top/bottom): X – light, U – dark.
Numeration of strips
left -> right: X1, X2, X4, X5, X7, U1,
U2, U3, U4, U5, U7;
right -> left: X3, X6, X8, U6, U8.
Thickness – 0.3 mm
Number of strips – 640
Pitch – 0,095 mm
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia
U-coordinate, ±2.5˚
8

## Slide 10
9
MiniSPD stand for testing Si-detectors
1
2
3
4
6
5
7
8
Top scintillator
bottom scintillator
We select events when top and bottom scintillators trigger.
One, two or three
Si-plates can trigger.
The simulation shows
that the scintillator response efficiency is close to 99.99 %.
tracks of muons
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 11
10
We compare our MC simulation of 50 000 muon tracks with experimental data (~ the same number) obtained from the operation of two scintillator triggers and Si-plates at the MiniSPD stand.
MiniSPD stand for testing Si-detectors
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 12
11
Strip number distributions for X1, X2, U1, U2 plates
X2 ~ 100 channels make enhanced noise
X1 - good work
good work
MC
DATA
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 13
12
Strip number distributions for X3, X4, U3, U4 plates
MC
DATA
U3 - noise channels
U4 - dead channels
X4 – there are noise channels
X3 ~ ½ of strips
don’t work
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 14
13
Lower registration threshold on energy
<ADC> ~ <Edep> (energy deposition in a single strip), the lower threshold of ADC ~ the lower threshold registration of energy deposition (E_cut). Using good planes (X1, X6, U2, U8) we get
30 keV < E_cut < 60 keV and its average value is equal ~ 55 keV.
Ed, MeV
ADC
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 15
14
Alignment from minimization of residuals of F
Reality
Nominal geometry
Aligned detectors
,
Large number of parameters: track parameters (4 * number of tracks)
and shifts(numbers of detectors), number of hits >> parameters.
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 16
15
Millipede procedure improves
χ2 distributions
Before alignment
After alignment
Shifts for part 5 (mm)
Result of fit for global parameters
===============
I initial final
--- ----------- -----------
1 0.00000 0.00000
2 0.00000 0.00000
3 0.02798 0.02841 - x-side
4 0.97531 0.97572 - u-side
5 0.00000 0.00000
6 0.00000 0.00000
Total 3428 local fits,
1335 rejected.
148-file
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 17
16
Result of fit for global parameters
- - - - - - - - - - - - - - - - - - - - - - - - - -
I initial final
----- ----------- -----------
1 0.00000 0.00000
2 0.00000 0.00000
3 -0.00378 -0.00365 - x-side
4 0.34720 0.34735 - u-side
5 0.00000 0.00000
6 0.00000 0.00000
- - - - - - - - - - - - - - - - -
Total 3558 local fits,
1409 rejected.
Millipede procedure improves
Shifts for part 4 (mm)
Before alignment
After alignment
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 18
17
Results
Monte Carlo simulation of double-sided silicon plates of miniSPD stand is carried out for two cases: with and without taking into account operation of the scintillator triggers.
Comparison of Monte Carlo simulation with experimental data allows to estimate the lower threshold on energy for a single strip operation.
Work of all parts (1-8) and their X and U sides of Si-detectors was analyzed and compared with MC simulation.
Noisy and dead channels are seen directly from the distributions according to the numbers of the triggered strips.
Alignment task is solved for the middle (II) module. The distributions on residuals of its parts and on tracks are obtained.
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 19
18
Outlook
We continue carrying out MC simulation of straw (drift) tubes to compare its with experimental data obtained at MiniSPD stand.
We also plan carrying out Monte Carlo simulation of the electromagnetic calorimeter work (8 modules).
It will allows us to start solving our basic task, studying (direct) soft photon yield and the pionic condensate formation (restoration of 𝜋0) in pp (pd, dd) interactions at high multiplicity.
https://www.youtube.com/watch?v=wCqX_rNi-60&feature=emb_imp_woyt
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 20
Backup
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 21
6
General layout of SPD setup
2102.00442[hep-ex]
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 22
Light Ion Linear Accelerator (LU-20)
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 23
5
Nuclotron – superconducting heavy ion accelerator
E. Kokoulina (kokoulina@jinr.ru)
MiniSPD stand for testing Si-detectors
NPCS, 21.06.22, Minsk, Belarus

## Slide 24
6
First magnet in collider’s tunnel
On 28 December last year, the first superconducting magnet was installed in the tunnel of the NICA accelerator complex. Moreover, a testing system of the MPD solenoid was launched. The magnet factory produces superconducting magnets not only for the NICA project but also for the German project FAIR. The next purchasers of Dubna magnets will be China and CERN.
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 25
12
Layout of silicon plates at MiniSPD stand
Z
X
Y
Our coordinate system
Modules of two-sided Si-plates: dark color indicates oblique (U, 2.5̊) strips, light - vertical (X) strips
The top (I) module consists of two parts: left (1) and right (2) plates
The middle (II) module consists of 4 parts. We numerate them 3, 4, 5 and 6 parts from left to right.
The bottom (III) module is similar to I with numeration of left and right: 7 and 8.
Two planes of
Straw tubes
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 26
26
Combinations of Si-modules for passing tracks
I
II
III
IV
N file
Comb.
N tracks
Vertical
tracks
Oblique
tracks
Low level
of noise
1
2
7
3
6
5
8
4
LLR
1 | +2.5
2 | +2.5
3 | -2.5
4 | +2.5
5 | +2.5
6 | -2.5
7 | -2.5
8 | +2.5
part, N
angle, deg
The same orientation for U-coord. is only for
148, 158, 248 combin.
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 27
14
Simulation of cosmic muons (170 MeV)
Polar angle () distribution by cosine
Azimuthal angle () - uniform distribution
𝞀 = < R = 10 cm - uniform distribution
𝞀 < 10 cm
- <
0 <
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 28
9
Simulation of triggered strips
Adding of StripStepping.cc to SteppingAction.cc
We use GEANT4 for simulation. In StripStepping for
every module and its parts:
Connect the triggered strip number with X-coordinate, define U-coordinate for the same plane, the strip number on U-plate and its E_dep (energy deposition).
Sorting of the triggered strip numbers in ascending order for elimination of repeating numbers (for X & U).
Accounting for crossing the border of the triggered strip when making a stepping.
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 29
15
Simulation of cosmic rays by Geant4 at theta = 50 deg.
miniSPD
z
y
x
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 30
Positioning of Si-plates
Plane | X, mm | Y, mm | Z, mm | Size, mm
X1, U1 | -28,55 | 0 | 35,0 | 63 x 126
X2, U2 | 31,55 | 0 | 50,3 | 63 x 126
X3, U3 | -32,55 | -27,55 | 387,8 | 63 x 63
X4, U4 | 27,55 | -32.55 | 395,1 | 63 x 63
X5, U5 | -27,55 | 32,55 | 395,1 | 63 x 63
X6, U6 | 32,55 | 27,55 | 387,8 | 63 x 63
X7, U7 | -28,55 | 0 | 893,5 | 63 x 126
X8, U8 | 31,55 | 0 | 886,2 | 63 x 126
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 31
20
Strip number distributions for X5, X6, U5, U6 plates
MC
DATA
X5 and X6 - good work
U5 ~1/4 channels
make noise
U6 - almost good
work
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 32
21
Strip number distributions for X7, X8, U7, U8 plates
MC
DATA
X7 – there are few noise channels
X8 – work
almost well
U7 – there are
some noise channels
U8 works well
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 33
13
ADC for X & U plates (* – issues with electronics)
*
*
*
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia
*
*

## Slide 34
E. Kokoulina (kokoulina@jinr.ru)
MiniSPD stand for testing Si-detectors
NPCS, 21.06.22, Minsk, Belarus
23
ADC for X & U plates (* – issues with electronics)
*
*
*

## Slide 35
28
Residual distributions
Before alignment
After alignment
X4
U4
U4
Parts 1,4,8
X4
X5
U5
Before alignment
Parts 1,5,8
After alignment
X5
U5
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 36
Access to intermediate and high values of Bjorken x
SPD is low energy but still collider experiment (compared to fixed target). Nearly 4π coverage
Two injector complexes available ⇒ mixed combinations p↑-d and p-d↑ are possible
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 37
SPD compared to other spin experiments
Main present and future gluon-spin-physics experiments
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 38
Tentative running plan for SPD (I stage)
Physics goal | Required time | Experimental conditions
Spin effects in p-p scattering dibaryon resonances | 0.3 year | pL,T - pL,T , < 7.5 GeV
Spin effects in p-d scattering, non-nucleonic structure of deuteron, yield | 0.3 year | d tenzor - p, < 7.5 GeV
Spin effects in d-d scattering hypernuclei | 0.3 year | d tenzor - d tenzor, < 7.5 GeV
Hyperon polarization, SRC, ... multiquarks | together with MPD | d tenzor - p, < 7.5 GeV
Spin effects in p-p scattering dibaryon resonances | 0.3 year | 
 | 0.3 year | 
Spin effects in d-d scattering hypernuclei | 0.3 year | 
Hyperon polarization, SRC, ... multiquarks | together with MPD | 
Total cost ~ 100 M$
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia

## Slide 39
Tentative running plan for SPD (II stage)
Gluon TMDs, SSA for light hadrons | 1 year | pT - pT , < 27 GeV
TMD-factorization test, SSA, charm production near threshold, onset of deconfinement, p ̄ yield | 1 year | d tenzor - p, < 27 GeV, (scan)
Gluon helicity, ... | 1 year | pL - pL, < 27 GeV
Gluon transversity, non-nucleonic structure of deuteron, ”Tensor polarized” PDFs | 1 year | d tenzor -d tenzor , = 13.5 GeV or/and d tenzor – pT, = 19 GeV
Gluon TMDs, SSA for light hadrons | 1 year | 
TMD-factorization test, SSA, charm production near threshold, onset of deconfinement, p ̄ yield | 1 year | 
Gluon helicity, ... | 1 year | 
Gluon transversity, non-nucleonic structure of deuteron, ”Tensor polarized” PDFs | 1 year | 
Physics goal | Required time | Experimental conditions
E. Kokoulina
MiniSPD test bench for testing of SPD detectors prototypes
6th ICPPA, Moscow, Russia