## Slide 1: Analog spectrometer of the DGFRS-2 setup: status and developments Yu.S.Tsyganov1, D.Ibadullaev1,2,3, A.N.Polyakov1, A.A.Voinov1, M.V.Shumeiko1 1- JINR, Dubna 2- INP, Almaty, 3- Humilev University, Astana
Introduction. Field of interest: Synthesis of SHE at the Dubna Gas-Filled Recoil Separator
New gas-filled separator (DGFRS-2)
New spectrometer complex of the DGFRS-2. Examples of application in HI induced nuclear reaction. Flexible scenario(algorithms) of “active correlations” method
SUMMARY
6th International Conference on Particle Physics and Astrophysics
* In more wide sense : collaboration FLNR(Dubna, Russia), ORNL( Oak Ridge, USA), IMP (Lanzhou, China)
Field of interest: Nucl. Phys. heavy ion induced complete fusion reactions->synthesis/properties SHE
detection system  RT algorithm of background signals suppression
-1

## Slide 2
History SHE in brief…
Z=114-118
The Dubna Gas Filled Recoil Separator
FLNR, JINR

## Slide 3: sum of technologies…
Cyclotron ~ 1 pµA…10 (48Ca beam, 50Ti,58Fe, 54Cr in a nearest future >5 pµA)
Actinide target (rotating) to apply high intensity for a long time
differential pumping system
Gas –Filled Separator ( to suppress primary beam and other backgrounds )
Detection system ( DSSD+ΔE(gaseous)+electronics + software(Builder C++) )
DGFRS-2
new Dubna Gas-Filled Recoil Separator
(since 2020)
DGFRS-1
DGFRS-2
factor of 3
DGFRS-1

## Slide 4: ΔE low pressure pentane-filled DGFRS#2 detector
Alpha 5.4
~8.2 ch
Z=114
EVR
background
240 mm x 60 mm
242Pu+48Ca287Fl+3n (~2..3 pµA)
`
Vc=-40, Va=+320 , VADD =-200 V
Cathode 20µ-1mm…
W(Au) wire @ expense ~4L/month liquid
D(a-c)~ 6 mm; ha =2 mm; hc=1mm
W(a)=20 µ; W(c) =10 µ.
..or..reverse order
~35-45 ~2y

## Slide 5
Block-diagramm of THE DGFRS#2 analog spectrometer
256 electronics channels
3 ΔE (in use 2)
+3 technological(counter 8in 16 bit)
+16 (reserved, not in use now)
subsystems: ΔE, RT (beam stop), SCP(3).
..others – standard spectrometry
In red – status register
∑=278 channels
4in/8out
0.2µs
TTL

## Slide 6
…for Dynamic Background Suppression.
Active correlations method
It means that:
To search for in a real-time mode pointer to a potential ER(implanted)-alpha correlation;
To create short break points in target irradiation; (def)short =
To detect forthcoming alpha decays (or even SF decay) in a background free mode, that is , when suppression factor in the value of probability to be a random decreases by several orders of magnitudes (6-9, usually, depending on number of chains).
Data flow
START
EXPERIMENT
End
Experiment
t1
Off- line
Data processing
(careful)
t2
ti
…
Short break points (pauses) in the target irradiation process 1,2…i..N
N
N(N-1)/2 graph edges
If N- number of nodes

## Slide 7: Implementation of the spectrometer…(view, few words, both..digital+analog)
digital
analog
Flange with DSSD, preamps…
Crate with splitters to branch the signals

## Slide 8
242Pu+48Ca287Fl+3n
EVR (287Fl)REGISTERED 100 events
dot – PC simulation
Yu.Tsyganov
NIM A 378(1996)
pp.356-359
Experiment | Time | Yield
243Am(48Ca,2-5n)286-289Mc | ~161 days | 125 decay chains
242Pu(48Ca,3-4n)286-287Fl | ~82 days | 94 decay chains
238U(48Ca,3n)283Cn | ~49 days | 16 decay chains
232Th(48Ca,3-4n)276-277Ds | ~82 days | ~6 decay chains

## Slide 9: Flexible algorithm- main idea…
to make the initial conditions more open…
“initial”
 ER (Emin, E max), (ΔEmin/max), tcorrER-α, tpause…
Standard mode :
Flexible mode:
tER-alpha=const (input file)
tiER-alpha=f(Nbi-1)
iterations
C++ on Timer

## Slide 10: 1) Natural (trivial) algorithm
n steps, 1 < n < N0 OR beam stop occurs
t0ER-a=1 s …tfinER-a=10 s
Beam off

## Slide 11: 2) Flexible scenario for RT background suppression method (probability)
Nb < N0 – one can consider as an optimization criterion;
It means, that, if (e.g.) Nb=10 and TPAUSE=100 s,
Then  beam loss value is equal to: 1000 s= 100*1000/24/3600=
0.12%
.. Is a very good compromise value!
To start this process 
In the YDA C++ code
press Button “Autopilot1”…
#1 Nb/day as an optimizing parameter,
Nb is “ER-α “ random correlation number expectation
June 2022
~4 pmcA
t0=50 ms...tfin=19,7 s
242Pu+48Ca287Fl+3n
Beam intensity ~ 1.6 pµA

## Slide 12: …few words about DSSSD (radiation) stability (itself, param’s)
// as a rough estimate…
Table 17 from p. 92
Three ref. points: p,α, FF
Base –
Wilkins formula for PHD
~5 months
of irradiation
48 front strips
U-400

## Slide 13
summary:
Long-term experiments were successfully performed with a new analog spectrometer
2) flexible scenario for ER-alpha sequences search algorithm has been tested during a few hours tests in the 48Ca beams up to ~7 pμA;
3) System is ready for nearest future experiments with 48Ca, 50Ti,54Cr projectile.
6th International Conference on Particle Physics and Astrophysics
FLNR

## Slide 14
The DGFRS-2 team 2020
Thank you for attention !
New discovery is
only a new discovery,
but, new methodology
is several new discoveries!
© Prof. V.V. Volkov (FLNR, JINR)
( star markers –MEPHI as Alma Mater)
There are no applied sciences,
there are only
applications of Science!
(L. Paster (?) )
The DGFRS-1 team; ~1999
All the new superheavy nuclei in the reactions
with 48Ca at JINR were discovered with
use of the DGFRS-1 alone !!!