## Slide 1
Low-pressure Time Projection Chambers for Experiments with Low-energy Ions
A. Bondar, A. Buzulutskov, V. Parkhomchuk,
A. Petroghitsky, T. Shakirova, A. Sokolov,
Budker Institute of Nuclear Physics,
Novosibirsk State University
December 2, 2022

## Slide 2
Outline
Accelerator mass spectrometry
New concept of ion identification. Proof of Concept
Experimental setup
Measurements of energy spectra and track ranges
TPC with optical readout

## Slide 3
Accelerator mass spectrometry
Accelerator mass spectrometry (AMS) is an ultra-sensitive method of counting individual atoms. Usually it is the rare radioactive atoms with a long half-life. The archetypal example is 14C which has a half-life of 5730 years and an abundance in living organisms of 10-12 relative to stable 12C isotope.
AMS facilities operate in more than 100 physical laboratories worldwide, one of which is located in Novosibirsk at Geochronology of the Cenozoic Era Center for Collective Use.

## Slide 4
1. Formation of an ion beam from atoms of the test sample
2. Ion selection at low energy
3. Ion acceleration
4. Recharging of atomic ions and destruction of molecular ions in magnesium target
5. Ion selection in a high voltage terminal
6. Ion acceleration
7. Ion selection at high energy
8. Identification and counting of ions
BINP AMS provides reliable separation of a pure beam of radiocarbon ions from the accompanying ion background.
BINP AMS

## Slide 5
Isotopes used in AMS
Analyzed isotopes | Half life | Stable isotopes | Stable isobars
10Ве | 1,39 million years | 9Be | 10B
14C | 5730 years | 12,13С | 14N*
26Al | 717 thousand years | 27Al | 26Mg*
36Cl | 301 thousand years | 35,37Cl | 36Ar*, 36S
41Ca | 102 thousand years | 40,42,43,44Ca | 41K
129I | 15,7 million years | 127I | 129Xe*
In the current AMS BINP setup the time-of-flight technique is used for the isotopes separation. But that technique there is a serious problem of separating the isobars - different chemical elements having the same atomic mass. The typical example are radioactive isotopes 10Be and 10B.
* - isobars that do not form stable negative ions.

## Slide 6
∆Е-Е detectors
A cross section through the multi-element ionization chamber. The upper panel shows a plan view of the anode electrode.
Detectors used to count the AMS isotope:
silicon detectors;
time-of-flight systems (BINP AMS);
ionization chambers.
Traditional concept of ion identification at AMS
6
Ions track lengths at 50 Torr of i-C4H10

## Slide 7
New concept of ion identification: low-pressure TPC
Schematic layout
Ion beam from AMS
or alpha particles
Si3N4 window
Ion track
Ionization
GEM
Anode
Charge-sensitive
preamplifiers
Cathode
Shaping amplifiers
Oscilloscope
Isobutane

## Slide 8
Proof of concept: measuring track ranges
SRIM (The Stopping and Range of Ions in Matter Software) –
is a collection of software packages which calculate many features of the transport of ions in matter.
Ion ranges distributions in the low-pressure TPC for alpha particles with different energies for 200 nm silicon nitride window and 50 torr isobutane, obtained using SRIM simulation.
Track ranges distributions in the low-pressure TPC for 4.025MeV 10B and 10Be ions for 200 nm silicon nitride window and 50 torr isobutane, obtained using SRIM simulation.

## Slide 9
pulse width track range
pulse area energy
Typical waveform shape of the signal from the alpha particle in low-pressure TPC
TPC Prototype: Principle of operation
Diameter – 178 mm
Length – 300 mm
178
300
233U, 238Pu, 239Pu
source

## Slide 10: Test installation appearance

## Slide 11
Effective gain of GEM
GEM effective gain as a function of the voltage in isobutane at pressures varying from 40 to 70 torr in the low-pressure TPC.
11
Electric field inside the holes.
50 µm

## Slide 12
The measurement of track ranges
The alpha-particle source
233U, 239Pu, 238Pu
Pressure = 50 Torr
Gain = 225
Shaping time = 200 ns
2D plot of pulse width versus pulse area and their axis projection spectra for alpha particles from 233U (4.8 MeV), 239Pu (5.2 MeV) and 238Pu (5.5 MeV) source, measured in low-pressure TPC in Isobutane at 50 Torr and GEM gain of 225.
The pulse width and pulse area spectra reflect those of the track range and energy.
12

## Slide 13
10B
10Be
Results
Source | Shaping time | Gain | Pressure | Sigma/Range, % | Separation in sigma between two peaks
3 isotopes | 200 ns | 225 | 50 Torr | 1.24 | 8
Using these results and SRIM code simulations, it is shown that isobaric boron and beryllium ions can be effectively separated at AMS, providing efficient dating at a 10 million years scale. This technique will be applied in the AMS facility in Novosibirsk.
Spectra of ion ranges for 10B and 10Be with energy 4.025 MeV in Isobutane at 50 Torr simulated with SRIM.
13

## Slide 14: TPC for BINP AMS
110 mm
70 mm

## Slide 15: TPC for BINP AMS

## Slide 16: Measuring reaction cross-section of p+11B → 3α + 8.7 MeV
https://tae.com
https://hb11.energy/
Neutronless Fusion Reaction
Large fuel reserves: 80% of natural boron – 11B isotop;
no radiation in energy production: no neutrons are produced, no problem of disposal of "activated" materials, no radioactive waste;
Direct production of electricity: reaction products are 3 α-particles.
TAE (Tri Alpha Energy) Technologies
Controlled fusion in a field reversed configuration and direct energy conversion.
“It aims to manufacture a prototype commercial fusion reactor by 2030.”
HB11 Energy
HB11 Energy aims to create a new source of clean, safe and reliable energy using laser technology to fuse Hydrogen and Boron-11.

## Slide 17: TPC with Optical ReadOut
Семинар секции плазмы ИЯФ
17
Version 1:
continuous beam
Lens Kowa
16 mm
Orca-flash 4.0
CMOS camera
p
E = 2 MeV
α
E = 1 MeV
α
E = 4 MeV
α
E = 4 MeV
Quartz window
Glass window
Gating grids
GEM
(anode)
Cathode
Si3N4
window
PMT
R11065
B(CH3O)3 (100 torr) + CF4 (150 torr)
PMT
R11065
Quartz window

## Slide 18: TPC with Optical ReadOut
Version 2
Pulse beam
Glass window
GEM
(anode)
Cathode
Si3N4
window
B(CH3O)3 (100 torr) or
B(CH3O)3 (100 torr) + He (150 torr)
p
E = 0.7÷1 MeV
α
E = 1 MeV
α
E = 4 MeV
α
E = 4 MeV
Beam killer
Lens Kowa
16 mm
Orca-flash 4.0
CMOS camera

## Slide 19: TPC with Optical Readout
Photo of assembly with the GEM, an optical window and the camera ORCA-Flash4.0;
Only one GEM has shown. In the final version, the triple GEM was used.
Size of GEM 10x10 cm2 fully matched with the camera matrix size 11x11 mm2. The spatial resolution in that case is about 50µm.
The maximum frame rate of the camera is 100 Hz.

## Slide 20: TPC with Optical Readout
TPC with the optical readout installed.
High voltage divider for the triple GEM is open.

## Slide 21: TPC with Optical Readout
Optical readout testing.
The sum of 100 consecutive frames with a shutter speed of 100 ms.
Gas amplification is about 1000.
Gas medium is pure CF4 with 300 Torr absolute pressure.

## Slide 22: Conclusion
A new concept of the detector for the accelerator-based mass spectrometer was proposed for identifying ions by their stopping range in gas;
A low-pressure TPC based on this concept have been made and successfully tested;
The TPC is ready for the installation on AMS;
The new idea of the optical readout from TPC was suggested and successfully tested;
The concept of two experiments with the use of the low-pressure TPC is proposed.

## Slide 23
Thank you for your attention!
23

## Slide 24
Backup slides
24

## Slide 25: Migdal effect
Looking for a rare (10-5) atomic phenomenon never before observed in the nuclear scattering
Migdal effect increases sensitivity of DM experiments to low mass WIMPs
Aim of the MIGDAL experiment - unambiguous observation and measurement of the Migdal effect using a low pressure Optical TPC
Signal signature: “V-like” shaped event with two tracks from electron and NR with different dE/dx and sharing the same vertex

## Slide 26: Simulated Migdal events in 100% CF4 at 50 Torr
Ionisation from electron using DEGRAD and full recoil cascade simulation using TRIM
150 keV Fluorine recoil and 7.5 keV electron
150 keV Fluorine recoils and 5 keV electron (secondary recoil clearly visible)
Secondary recoil
Electron
Primary recoil

## Slide 27
Formation and application 10Be
Application in-situ and
meteoric 10Be:
exposure dating to identified the growths and decays of the Antarctic ice sheet;
understanding ice shelf collapse history;
paleomagnetic excursions history reconstructions using ice cores;
understanding the erosion rates using depth profiles of mid latitudes outcrops;
identifying the timing of formation of the impact crater and so forth.
Time intervals of dating:
14C from 300 years to 40-60 thousand years
10Be from 1 thousand years to 10 million years

## Slide 28
Measurements of energy spectra using semiconductor detector
Alpha particle source– 233U, 239Pu , 238Pu
Energy spectrum of alpha particles from 233U (4.8 MeV), 239Pu (5.2 MeV) and 238Pu (5.5MeV) sources, measured using semiconductor detector
Si Charged Particle Radiation Detectors for Alpha Spectroscopy
28

## Slide 29
The measurement of track ranges
The alpha-particle source
233U, 239Pu, 238Pu
Pressure = 50 Torr
THGEM Gain = 67
Shaping time = 200 ns
29
2D plot of pulse width versus pulse area and their axis projection spectra for alpha particles from 233U (4.8 MeV), 239Pu (5.2 MeV) and 238Pu (5.5 MeV) source, measured in low-pressure TPC in Isobutane at 50 Torr and THGEM gain of 67.
The pulse width and pulse area spectra reflect those of the track range and energy.

## Slide 30
Silicon nitride membrane windows
M. Dobeli et al., Nucl. Instr. and Meth. B, 219-220 (2004) 415-419 doi:10.1016/j.nimb.2004.01.093
Figure of silicon nitride membrane windows
30

## Slide 31
Схема УМС ИЯФ:
1 – ускорительная трубка, 2 – бак ускорителя, 3 – электростатический поворот на 180°, 4 – магниевая мишень, 5 – корректор, 6 – электростатическая линза, 7 – вакуумный насос, 8 – детектор ионов, 9 – дипольный магнит спектрометр на высокой энергии, 10 – дипольный магнит спектрометр на низкой энергии, 11 – ионный источник.
Характерные особенности УМС ИЯФ:
мишень на парах магния для разрушения молекул локализованное место развала молекул;
сортировка ионов по энергии сразу после разрушения молекулярных ионов эффективное отсеивание осколков молекул, т.к. энергия кусков молекулы всегда меньше энергии молекулы;
времяпролетный детектор с регистрацией момента прилета ионов.
BINP AMS
31