## Slide 1
A. Lukanov, V. Gavrin, A. Fazliakhmetov, T. Ibragimova, B. Lubsandorzhiev, D. Nanzanov, A. Shikhin, A. Sidorenkov, N. Ushakov, D. Voronin
Baksan Large Neutrino Telescope project
ICPPA, 2022

## Slide 2: Main goals of the project
Geoneutrino flux measurements
Registration of neutrinos from the Sun’s CNO cycle
Registration of isotropic flux of antineutrinos accumulated in the Universe as a result of gravitational collapses of the nuclei of massive stars and the formation of neutron stars and black holes
Study of a supernova explosion by recording the intensity and spectrum of a neutrino burst in the case of a supernova explosion with a collapsing core
Registration of total antineutrino flux from all nuclear power reactors
A number of applied tasks, such as promotion for a revival of development and production of vacuum and solid state photodetectors in Russia

## Slide 3: Project stages
First stage - prototype with 0.5 tons of liquid scintillator located in gallium-germanium neutrino telescope (GGNT) laboratory of Baksan Neutrino observatory (BNO)
Second stage - prototype with 5 tons of liquid scintillator also located in GGNT laboratory. Testing of applied scientific and technical methods
Third stage - detector with ≈100 tons of liquid scintillator
Fourth stage - detector with 10 kTons of liquid scintillator, which could solve whole range of project goals

## Slide 4: Location of Baksan neutrino observatory
Andirchi Mountain
Baksan Neutrino observatory and v. Neutrino
4

## Slide 5: Map of nuclear power plants location
ICPPA, 2022
5
Borexino
BNO
JUNO
Jinping
KamLAND
SNO+

## Slide 6: Reactor neutrino flux in GGNT laboratory
Location | Geoneutrino flux, TNU | Reactor neutrino flux in geoneutrino range, TNU | Nreact/Ngeo
BNO | 50.8 | 13.2 | 0.26
Gran Sasso (Borexino) | 40.7 | 23.2 | 0.57
Kamioka (KamLAND) | 34.5 | 43.7 | 1.27
Sudbury (SNO+) | 50.8 | 51.7 | 1.02
Jinping | 59.4 | 5.6 | 0.09
Pyhasalmi | 51.5 | 19.4 | 0.38
Hawaii | 12.5 | 1.1 | 0.09
JUNO | 39.7 | 307.8 | 7.75
Energy, MeV
Energy, MeV
Flux, TNU/MeV
Flux, MeV-1cm-2s-1
ICPPA, 2022
6

## Slide 7: Supposed construction of Large volume detector
Liquid scintillator
Buffer zone filled with non-scintillating organic liquid
Transparent reservoir
Radon protection
PMTs
Non-transparent reservoir
Water (Cherenkov detector)
Linear alkyl benzene (LAB)
10kT
ICPPA, 2022
7

## Slide 8: First stage of the project
Polypropylene water reservoir
Stainless steel frame
Twenty 10-inch PMTs Hamamatsu R7081-100 WA-S70
Scintillator is contained within acrylic sphere with a radius 0.5 m
ICPPA, 2022
8

## Slide 9
ICPPA, 2022
9

## Slide 10: Liquid scintillator
Liquid scintillator is based on linear alkyl benzene with added 2 g/l of PPO and 10 mg/l of bis-MSB
LAB is produced by Ltd KINEF
Wavelength, nm
Emission spectrum of PPO in LAB
Emission spectrum of bis-MSB in toluene
Plexiglass transparency spectrum
Transmission/
Emission intensity, %
ICPPA, 2022
10

## Slide 11: Registration system
PC
High voltage power supply
PMT
Discriminator
Amplifier
Signal
Digitizer
Trigger
Sampling rate: 500 MS/s
Dynamic range: 2 V
Resolution: 14 bit
Buffer size: to 2 ms
Coincidence circuit
Veto system
Scaler
Programmable logic module V2495
VMEbus
Dividing panel
ICPPA, 2022
11

## Slide 12: PMT Hamamatsu R7081-100 WA-S70
Parameter | Value
Dark current pulses | 1.74±0.87
Peak-to-valley | 3.73±0.56
SPE resolution | 0.68±0.06
Jitter | 3.01±0.24
Wavelength, nm
Quantum efficiency, %
Relative light yield
Quantum efficiency spectrum of PMT
Light yield spectrum of PPO
Light yield spectrum of bis-MSB in toluene
ICPPA, 2022
12

## Slide 13: Second stage of the project
50 m3 stainless steel water reservoir
Forty two 10-inch PMTs Hamamatsu R7081-100 WA-S70
Acrylic sphere with 1.1 m radius
ICPPA, 2022
13

## Slide 14
Muon detector based on plastic scintillator and silicon photomultiplier
Magnetic field compensation system
Light absorbing film for separation of scintillation target and Cherenkov detector
Carbon light concentrators
Twelve 8-inch PMTs Hamamatsu R5912-100 WA-S70 for muon water Cherenkov detector
ICPPA, 2022
14

## Slide 15: Scintillator purification
LAB purification by sorption with Al2O3
LAB and PPO purification from potassium by water extraction
ICPPA, 2022
15

## Slide 16: Earth magnetic field compensation system
Measured values of magnetic field in prototype location:
horizontal component – 0.265 G, vertical – 0.25 G
Horizontal component: Number of coils 12
Turns = 7
Vertical component: Number of coils 5
Turns = 10
ICPPA, 2022
16

## Slide 17: Results
First stage is completed
-Muon flux has been measured ((4.02±0.24)*10-9 cm-2s-1)
-Radioactive background of prototype materials has been measured
-Energy detector response was 172.6 photoelectrons/MeV after calibration by radioactive sources
Acrylic sphere, steel frame and steel water reservoir has been made
6 tons of LAB have been purchased, scintillator purification system has been developed
Characteristics of 10-inch and 8-inch PMTs have been measured
Optimal shape of light concentrators has been calculated, test concentrator has been produced
Earth magnetic field compensation system has been developed
ICPPA, 2022
17