## Slide 1
ICPPA 2020
October 4-11
Russia Moscow
Andrey
Konstantinov
NRC Kurchatov institute
Status
of the iDream project

## Slide 2
iDream team
Currently there is a collaboration of NRC Kurchatov Institute and Skobeltsyn Institute for Nuclear Physics (Lomonosov Moscow State University):
  NRC Kurchatov Institute: A. Abramov, A. Chernov, A. Etenko, A. Konstantinov, D. Kuznetsov, E. Litvinovich, G. Lukyanchenko, A. Murchenko, A. Nemeryuk, R. Nugmanov, B. Obinyakov, A. Oralbaev, A. Rastimeshin, M. Skorokhvatov, S. Sukhotin.
  SINP MSU: A. Chepurnov, M. Gromov, K. Zamogilny.

## Slide 3
Prospects for the development
of neutrino monitoring
- Determination of the operational condition reactor (on or off) can be detected within 5 hours of shutdown or start-up with 99% confidence
- Determination of the current / daily reactor thermal power
- Determination of fission fractions of U and Pu isotopes in the reactor core
- Remote confirmation of the technogenic nature of a nuclear explosion
- Technically our detector has the ability to transmit registration data remotely, so in the future we can detect any reactor shutdowns and exclude nuclear proliferation of materials remotely

## Slide 4
A. Bernstein et al., Nuclear Security Applications of Antineutrino Detectors: Current Capabilities and Future Prospects, Science & Global Security, 18:127–192, 2010.
Different approaches of Reactor Safeguards

## Slide 5
STEREO
NEOS
PROSPECT
DANSS
iDream
and other projects
Applications of Antineutrino Detectors for Security

## Slide 6
Reference: https://vashurok.ru/articles/2019-10-24-pochemu-aes-samye-ekol
Our detector is:
- Structurally simple
- High-maintainability
- Easily-dismountable
and easy-to-assemble.
iDream is expected to be easily mounted at the plant
Top only location of the PMTs guarantees quick access for their removal/repair, if needed
iDream – industrial Detector of Reactor Antineutrinos for Monitoring

## Slide 7
The detector design has radiation protection
working condition
for setting up the detector

## Slide 8
Gd improves the efficiency of
neutron detection.
Using Gd-loaded LAB-based liquid scintillator
Inverse beta-decay reaction:

## Slide 9
Exclusion of data falsification
Registration of detector data should prevent falsification of physical data by external influences on the detector.
iDream
No falsification!

## Slide 10
iDream has the ability remotely to transmit registration data via communication channels to the remote control center.
Remote detector control

## Slide 11
The detector must work independently 24/7/365
No iDream service
Only autonomy

## Slide 12
Built-in calibration tools
of iDREAM detector
137Cs decay
207Bi decay
iDREAM detector
calibration scheme:
1 - engine source
2,3 - calibration
source position
The calibrations were performed along
z-axis (in the range -400 / +400 mm).

## Slide 13
The mathematical model (Geant4 based Monte Carlo method) showed good agreement with the calibration data at about 1%.
The latest results of calibrations
Detector was filled scintillator with LAB+PPO+bis-MSB

## Slide 14
Positron spectrum
Detector response has been simulated in the antineutrino flux (Huber-Mueller model), 19m from the VVER-1000 reactor core.

## Slide 15
Expected change in the rate of the antineutrino interaction in the target as a result of Pu-239 accumulation.
Comparative change of the antineutrino count rate:
the beginning (239Pu=0.25), middle (239Pu=0.33), and end of the campaign (239Pu=0.40).
Comparative change of the antineutrino
count of accumulated 239Pu
Chart: 
| Строка 1 | Строка 2 | Строка 3 | Строка 4
Столбец 1 | 9.1 | 2.4 | 3.1 | 4.3
Столбец 2 | 3.2 | 8.8 | 1.5 | 9.02
Столбец 3 | 4.54 | 9.65 | 3.7 | 6.2

## Slide 16
Last calibration data with/without lumir
For the detector with target fully coated by the Lumirror, we achieved the light collection inhomogeneity (-9%; +12%) - for (-400; +400) mm part of the target along z-axis.

## Slide 17
- The industrial detector iDream must be an IAEA tool for non-proliferation safeguards
- The ability to constantly monitor the use of fissile materials in real time
- The ability of a State to control its nuclear materials independently on international operating companies
- As a result: improving the operational safety of nuclear power plants
iDream is on the
international arena
Prospects for the development of neutrino monitoring for IAEA

## Slide 18
- The detector is being prepared for commissioning at Kalinin nuclear power plant, start of data taking planned for 2021
- Detector calibrations with gamma-sources have been performed
- The Monte-Carlo model of the detector showed good agreement with the calibration data - about 1%
- The light collection inhomogeneity was studied with the calibration data: for cylindrical part of the detector’s target (-400; +400) mm along z-axis we achieved (-9%; +12%) inhomogeneity
- Positron response of the detector in the antineutrino flux, 19m from the reactor core, was simulated; estimation of the expected change in the rate of the antineutrino interactions during the reactor campaign was obtained
Summary

## Slide 19
The end