## Slide 1
Universal Main Magnetic Focus Ion Source: A New Tool for Laboratory Astrophysics and Tokamak Microplasma Research
a MaMFIS group, Hochchulstr. 13, D-01069 Dresden, Germany
b Petersburg Nuclear Physics Institute, 188300 Gatchina, Russia
Vladimir P. Ovsyannikov,a Andrei V. Nefiodov,b Aleksandr A. Levina

## Slide 2
History
Production of highly charged ions
Electron Beam Ion Source (EBIS), E.D. Donets, Dubna, 1967
Ltrap= 0.7 – 1.5 m
je ~ 500 A/cm2
K, cathode
W, focusing (Wehnelt) electrode
A, anode
S1, S2,…, Sn, sections of drift tube
C, collector
E, extractor
z, axis of electron beam
je , effective electron current density
Ltrap , trap length

## Slide 3
History
Production of highly charged ions
Electron Beam Ion Trap (EBIT), M. Levine, R. Marrs, LLNL, 1986
EBIT + EXTRACTION = EBIS
K, cathode
W, focusing (Wehnelt) electrode
A, anode
S1, S2, S3, sections of drift tube
C, collector
E, extractor
z, axis of electron beam
je , effective electron current density
Ltrap , trap length
Ltrap= 2 cm
je ~ 2 kA/cm2

## Slide 4
History
Superconducting EBITs: design
The LLNL Super-EBIT (1992)
Lawrence Livermore National Laboratory
The LLNL EBIT (1986)

## Slide 5
Family of room-temperature
Dresden Electron Beam Ion Sources
Dresden EBIS-A
Dresden EBIS
Dresden EBIT
DREEBIT GmbH

## Slide 6
Dresden EBIS/Ts with permanent magnet focusing system
Germany Poland Swiss China
TU Dresden Jan Kochanowski University, Kielce PSI, Villigen NAOC, Beijing
FZ Dresden-Rossendorf Jagiellonian University, Krakow
Friedrich Schiller University, Jena
University of Duisburg-Essen
GSI, Darmstadt
MPI for Nuclear Physics, Heidelberg
Siemens AG Erlangen
Other permanent magnet EBITs around the Globe
USA Germany China
NIST, Gaithersburg MPI for Nuclear Physics, Heidelberg Fudan University, Shanghai

## Slide 7
Main Magnetic Focus Ion Source (MaMFIS)
K, cathode
W, focusing (Wehnelt) electrode
A, anode
C, collector
E, extractor
z, axis of electron beam
je , effective electron current density
Ltrap , trap length
Production of highly charged ions
Ltrap= 1 mm
je > 10 kA/cm2

## Slide 8
Formation of local ion traps by rippled electron beam
Sag of radial potential
Depth of axial potential well (local ion trap)

## Slide 9
Theoretical prediction of ion yields
Ar
Xe
Ne
Ion yield
Xe44+ : 2x106 ions/s (f = 100 Hz)
Ar16+ : 3x107 ions/s (f = 100 Hz)
Ar18+ : 106 ions/s (f = 50 Hz)
Ne10+ : 108 ions/s (f = 0.5 kHz)
Ne8+ : 109 ions/s (f = 1 kHz)

## Slide 10
CoBIT (N.Nakamura et al., RSI 79 (2008) 063104)
Ie = 20 mA,
U b 0.1 - 2.5 kV,
T = 77 K
EUV spectra of Fe ions obtained with CoBIT
Solar satellite
HINODE with
spectrometer EIS
Fe13+spectrum
by
HINODE
T. Watanabe et al. Ap. J. (2009)

## Slide 11
MaMFIS-4 with radial extraction of ions
Principal scheme of ion source
Ie = 50 mA, U b 0.1 - 4 kV,
je ~ 10 kA/cm2
T = 300 K
CoBIT (N.Nakamura et al., RSI 79 (2008) 063104)
Ie = 20 mA, U b 0.1 - 2.5 kV,
T = 77 K

## Slide 12
MaMFIS-4: x-ray emission measurements
Basic x-ray spectrum of Ir and Ce ions
Emission due to radiative recombintion

## Slide 13
UniMaMFIS
A. MaMFIS running mode
Magnetic field at the cathode Bc is zero.
The cathode-anode distance is equal to d1 for high-voltage ionization in a local ion trap with extremely high electron current density (je >= 10 kA/cm2).
B. EBIT running mode
Magnetic field at the cathode Bc is of a significant value.
The cathode-anode distance is equal to d2 for low-voltage ionization in the potential ion trap with relatively low current density (10 A/cm2 <= je <= 100 A/cm2

## Slide 14
Universal MaMFIS
Project parameters:
Operational regime | EBIS | MaMFIS
Ee (eV) | 200 – 12 000 | Up to 60 000
Ie (mA) | 10 – 200 | 200
je (A/cm2) | 20 – 500 | 20 000
Ltrap (cm) | 2 | 0.1
Expected yield of Xe52+ ~ 300 ions per second

## Slide 15
Pilot exemplar of UniMaMFIS
Pilot example of the device has been designed for two positions of cathode at 8.5 kV and 30 kV voltages of electron gun. The first measurements of X-ray emission spectra from cathode material were performed at the Institute for Atomic and Molecular Physics of the Justus-Liebig-University Giessen in Germany.

## Slide 16
UniMaMFIS in mode of MaMFIS-10 versus LLNL superconducting EBIT
M.A. Levine, R.E. Marrs,
J.R. Henderson, D.A. Knapp,
M.B. Schneider,
Phys. Scripta T22, 157 (1988)
LLNL EBIT
V.P. Ovsyannikov, A.V. Nefiodov,
NIMB 370, 32 (2016)
MaMFIS-10
First run: Giessen, March 2013

## Slide 17
UniMaMFIS running as MaMFIS-10: determination of electron beam current density
Electron current density je ~ 20 kA/cm2
X-ray emission due to radiative recombination into M-shell of Ir ions

## Slide 18
UniMaMFIS running as MaMFIS-10: control of local ion trap
Axial extraction of highly charged ions
from local ion trap is feasible
X-ray spectra measured in trapping and extraction modes

## Slide 19
Applications of highly charged ions
Accelerators (charge breeding, nuclear physics, cancer therapy)
Atomic physics (ion-atom collisions and x-ray spectroscopy)
X-ray astrophysics and solar physics
Extreme ultraviolet lithography
Plasma physics (magnetic fusion diagnostics)
Interaction of ions with surface (secondary electron and ion emission)
Secondary ion mass spectrometry
Nanostructuring
http://yebisu.ils.uec.ac.jp/surface.html
E. Akcoeltekin et al.,
Nature Nanotechnology 2, 290 (2007)

## Slide 20
High density microplasma research
MaMFIS:
Ee ~ 10 keV
je ~ 20 kA/cm2
ne ~ 2x1013 cm-3
Ee ~ 40 keV
je ~ 200 kA/cm2
ne ~ 1014 cm-3

## Slide 21
Summary
Novel method for the production of highly charged ions in rippled electron beam is developed and confirmed experimentally
Electron beam current density of about 20 kA/cm2 is achieved, what allows to model experimentally the microplasma characterized by high density close to that in tokamak
Method allows to produce any ions of arbitrary elements of the periodic table up to U92+ ions in simple compact devices
X-ray spectroscopy of all elements of the periodic table is feasible
Novel devices for nanostructering and surface analysis can be developed

## Slide 22
Acknowledgements
The authors express deep gratitude
to A. Mueller for giving opportunity to test MaMFIS in the laboratory of IAMP (Justus Liebig University Giessen),
to O. K. Kultashev for his contribution to creation of electron optics,
to I. V. Kalagin for his contribution for development of computer codes and
to A. V. Nukin for production of some details of MaMFIS.
THANK YOU FOR YOUR ATTENTION !