## Slide 1: Data acquisition system of the NEVOD-EAS array
The 2nd International Conference on Particle Physics and Astrophysics
(ICPPA-2016)
Moscow, Russia, October 10 - 14, 2016
O.I. Likiy1, M.B. Amelchakov1, N.V. Ampilogov1, I.I. Astapov1, D.S. Brovtsev1,
A. Chiavassa2,3, D.M. Gromushkin1, N.N. Kamlev1, S.S. Khokhlov1, K.G. Kompaniets1, A.S. Mazhuto1, V.V. Ovchinnikov1, O. Saavedra2, P.V. Semov1,
I.A. Shulzhenko1, I.I. Yashin1
1 National Research Nuclear University MEPhI, Scientific and Educational Center NEVOD, Moscow, Russia
2 Dipartimento di Fisica dell’ Università degli Studi di Torino, Turin, Italy
3 Sezione di Torino dell’ Istituto Nazionale di Fisica Nucleare - INFN, Turin, Italy

## Slide 2
NEVOD-EAS array

## Slide 3
Cluster of the NEVOD-EAS array

## Slide 4: Scintillation counter of the NEVOD-EAS array
Scintillator:
NE102A 80 × 80 × 4 cm3
Photomultiplier:
Philips XP3462
Most probable response to 1 particle (VEM): ~ 13 pC
Upper limit of dynamic range (with standard PMT): 100 particles VEM
Upper limit of dynamic range (with additional PMT): 104 particles/m2

## Slide 5: Detector Station (DS) of the NEVOD-EAS array
4 PMTs (standard): measuring EAS particle densities and time measurements.
5th PMT (additional): a gain of ≈ 90 times less than for the standard PMT; ensures wide linearity range of measured signals at high particle densities.

## Slide 6: Local Post (LP) of the NEVOD-EAS cluster
Local Post tasks:
- summation of standard PMTs signals;
- digitizing of PMTs signals;
- event selection according to triggering conditions;
- operation in exposition and monitoring modes;
- DS power supply;
- control of temperature inside DS and LP.
Local Post
Summator - Multiplexer
BAA
DS Power Supply
Thermal Relay
PET-7019
Media converter
DS
Controller

## Slide 7: Central DAQ Post
Central DAQ Post tasks: - cluster synchronization;
- cluster control;
- reception and storage of experimental
and monitoring data.

## Slide 8: Central DAQ Post

## Slide 9
Central part of the NEVOD-EAS array
Clusters No. 1 & 2
13.3×12.4 m2
Cluster No. 3
25.1×18.9 m2
Cluster No. 4
15.0×15.0 m2

## Slide 10: Conclusion
In 2015–2016 the central part of the NEVOD-EAS cluster type shower array which includes 4 independent clusters (totally, 64 scintillation counters) located around the Experimental Complex of the CWD NEVOD and coordinate detector DECOR at the area of about 104 m2 has been created and started.
The distributed structure of the NEVOD-EAS array DAQ system allows to deploy registering elements of the setup even at different altitudes and provides implementation of a newly developed cluster approach to the reconstruction of EAS parameters.
Our plans:
2016–2017
2018–2020
- start of operation of the 1st stage of the NEVOD-EAS peripheral part (+ 6 clusters, total area ~ 2×104 m2)
- start of operation of the 2nd stage of the NEVOD-EAS peripheral part (total area ~ 0.2 × 106 m2)

## Slide 11
Thank you for attention!