## Slide 1: ICPPA-2016
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Novelties in Elementary Particle
Gaseous Detectors
Technology
Fulvio Tessarotto
INFN - Trieste

## Slide 2: outline
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Historical introduction
Micromegas
GEMs
Novel detectors
Gaseous photon detectors
Conclusions

## Slide 3: Glorious tradition: 100 years of gaseous detector developments
1908: FIRST WIRE COUNTER
USED BY RUTHERFORD IN THE STUDY OF NATURAL RADIOACTIVITY
E. Rutherford and H. Geiger , Proc. Royal Soc. A81 (1908) 141
1928: GEIGER COUNTER
SINGLE ELECTRON SENSITIVITY
H. Geiger and W. Müller, Phys. Zeits. 29 (1928) 839
1911: CLOUD CHAMBER
Nobel Prize in Chemistry in 1908
Walther Bothe
Nobel Prize in 1954
Hans Geiger
Ernst Rutherford
Charles T.R. Wilson
Nobel Prize in 1927
COINCIDENCE METHOD
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 4: Glorious tradition: 100 years of gaseous detector developments
SPARK CHAMBER
1968: MULTIWIRE PROPORTIONAL CHAMBER
G. Charpak
G. C. Santiard
F. Sauli
1952: BUBBLE CHAMBER
Donald A. Glaser
Nobel Prize in 1992
George Charpak
Nobel Prize in 1992
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 5: Glorious tradition: 100 years of gaseous detector developments
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 6: GASEOUS DETECTORS
ATLAS, m spectrometer
Still today the only way to equip large volumes at a
reasonable cost, with good space resolution and
limited material budget
was the only approach to achieve good space resolution before introducing the Si trackers
Time resolution record in
extended counters
RPC: st ≤1 ns
trigger in ALICE, ATLAS, CMS
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 7: MWPCs
Extraordinary success and ubiquitous use of MWPCs:
in many discoveries they played an essential role
Even the best wires (Au coated, Rhenium/Tungsten) with a diameter of 5 µm cannot hold the tension needed to operate a 10 cm long MWPC.
To increase the rate capability: reduce the cell size
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 8: After MWPCs
Advantages of gas detectors:
low radiation length
large areas at low price
flexible geometry
space and energy resolution
The MWPC limits in:
- rate capability (space charge  E distortion)
- space resolution (cell size limitation)
- time resolution (signal from ion drift)
- aging
have been overcome by a change in technology since the anode is no more self supporting: strip on insulating substrate, …
Amplifying cell
size reduction by
factor of 10

## Slide 9
MicroStrip Gas Chamber
A. Oed, Nucl. Instr. and Meth. A263 (1988) 351.
Semiconductor industry technology:
Photolithography
Etching
Coating
Doping
Typical distance between
wires limited to 1 mm
Typical distance
between anodes 200 mm
thanks to semiconductor
etching technology
MWPC
MSGC
In the early days:
high E-values at the edge between insulator and strips  damages
Charge accumulation at the insulator  gain evolution vs time
Later (~ 1999-2000):
Passivation of the cathode edges
 MSGC operational
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 10
Telescope of 32 MSGCs tested at PSI in Nov99 (CMS Milestone)
HERA-B Inner Tracker
MSGC-GEM detectors
Rmin ~ 6 cm
 106 particles/cm2•sec
300 mm pitch
184 chambers: max 25x25 cm2
~ 10 m2; 140.000 channels
The D20 diffractometer MSGC
is working since Sept 2000
1D localisation
48 MSGC plates (8 cm x 15 cm)
Substrate: Schott S8900
Angular coverage : 160° x 5,8°
Position resolution : 2.57 mm ( 0,1°)
5 cm gap; 1.2 bar CF4 + 2.8 bars 3He
Efficiency 60% @ 0.8 Å
ILL Grenoble
DIRAC
4 planes MSGC-GEM
Planes 10x10 cm2
MSGC – MicroStrip Gas Chamber
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
HIROYUKI TAKAHASHI - Tokyo University
Collaboration with SHARP
transparent Single-grid-type MSGC based on LCD technology
8 um wide Anode
20um wide Grid
62 um Cathode
150 um pitch
2,000 billion € / year
SHARP

## Slide 11
MICRO-GAP CHAMBER
MICRO-GROOVE CHAMBER
MICRO-WIRE CHAMBER
COMPTEUR A TROUS
MICRO-PIXEL CHAMBER
MICRO-PIN ARRAY
Several different MPGDs have been developed

## Slide 12: MPGD
MICRO MEsh GAseous Structure (MICROMEGAS)
Thin gap Parallel Plate Chamber: micromesh stretched over readout electrode.
Y. Giomataris et al., Nucl. Instr. and Meth. A376(1996)29
GAS ELECTRON MULTIPLIER (GEM)
Thin, metal-coated polymer foil with high density of holes, each hole acting as an individual proportional counter.
F. Sauli, Nucl. Instrum. Methods A386(1997)531
2 very solid, fully established technologies:
HIGHER LUMINOSITIES, HIGHER PRECISION EXPERIMENTS
MPGDs allow for
  High rates (granularity & occupancy, signal formation time)
  Fine space resolution
Technological maturity and accurate engineering FUNDAMENTAL for successful MPGDs
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 13: operational in COMPASS since 2002
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 14: Micromegas
High voltage [V]
350
450
400
500
550
600
650
103
102
104
105
105
gain
gain
energy res. ~ 10%
55 Fe
Ar + 10% C4H10
Micromesh mounted above readout
structure (typically strips).
E field similar to parallel plate detector.
Ea/Ei ~ 50 to secure electron transparency
and positive ion
backflow supression.
1
0.9
0.8
0.7
0.6
10-4
10-5
10-6
10-7
10-8
discharge probability
efficiency
efficiency & discharge probability
High Voltage [V]
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 15: Standard Micromegas
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
s = 9 ns
s =70 µm

## Slide 16: Bulk Micromegas technology
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
woven mesh

## Slide 17: Resistive Micromegas
Screen Printed Resistive Layer for ATLAS
Assembly … as important as the micro structure .. If you want to preserve the properties at large scales
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
ATLAS – MM
New Small Wheel,
1200 m2
tracking & trigger

## Slide 18: Micromegas with resistive strips
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
in Japan a different production
method:
Resistive pads:

## Slide 19: Microbulk technology
Copper Etching
Kapton Etching
Kapton micro-bulk
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 20: INGRID
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 21: Timing with MPGD
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Using Cherenkov photons
Efficiency is very high
Time resolution much lower than 100 ps
hope to achieve 30 ps or better.

## Slide 22
GEM
Thin metal-coated polymer foil pierced by a high density of holes (50-100/mm2)
Typical geometry: 5 mm Cu on 50 mm Kapton, 70 mm holes at 140 mm pitch
70 µm
140 µm
Electrons
Ions
60 %
40 %
70 µm
55 µm
5 µm
50 µm
Induction gap
e-
e-
I+
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 23
50 mm Kapton
5 mm Cu both sides
Photoresist coating, masking and exposure
to UV light
Metal etching
Kapton etching
Second masking
Metal etching
and cleaning
Rui De Oliveira CERN-EST-DEM
GEM Manufacturing
GEM foils are produced at
CERN using proprietary process.
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 24
GEM – Gas Electron Multiplier
A. Bressan et al, Nucl. Instr. and Meth. A425(1999)254
Full decoupling of the charge amplification
structure from the charge collection and
readout structure.
Both structures can be optimized
independently !
Most of the detectors use three GEM foils in cascade for amplification
to reduce discharge probability by reducing field strength.
Cartesian
Compass, LHCb
Small angle
Hexaboard, pads
MICE
Mixed
Totem
Different flat shapes
cylindrical
spherical

## Slide 25
Multi-GEM Detectors are operated in discharge free mode
Discharge Probability on Exposure to 5 MeV Alphas
Multiple structures provide equal gain at lower voltage.
S. Bachmann et al Nucl. Instr. and Meth. A479(2002)294

## Slide 26: GEMs, spacers & stretching
TOTEM
60 cm
B. Ketzeret al, NIMA A535 (2004) 314
COMPASS
KLOE2: Triple cylindrical GEM
assembly completed 14/3/2013
LHCb
CMS upgrade:
mechanical
stretching
for mass
production
GEM detectors w/ spacers
Emphasis on GEM foils stretching
no spacers
no spacers
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 27: HIGH RATE applications
Pixelised GEMs (COMPASS)
stable operation in particle flux up to 1.2·105/s/mm2
extremely thin: 0.2% X0
spatial resolution: 90 μm
Austregesilo et al.,
NP B PS 197 (2009) 113
Hybrid GEM + Micromegas
GEM pre-amplification:
control the discharge
rate in tracking
MM w GEM pre-amplification
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 28
Large area single Mask GEM
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 29: Large GEMs at LHC
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 30: WELL and μ-RWELL
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Drift/cathode PCB
Copper top layer (5µm)
DLC layer (0.1-0.2 µm)
R ̴50 -100 MΩ/□
Rigid PCB readout electrode
Well pitch: 140 µm
Well diameter: 70-50 µm
Kapton thickness: 50 µm
1
2
3
µ-RWELL PCB
G. Bencivenni et al., 2015_JINST_10_P02008
Motivation: higher stability under intense irradiation and simplified construction
top copper layer
HV
kapton
kapton
r
t

Principle of operation:

## Slide 31: NOVEL ARCHITECTURE
mPIC
25μm
25μm
Anode
Resistive
film
Cathode
E-field will be dropped by spark current.
Resistive mPIC
A.Ochi and T.Tanimori,
NIMA 471 (2001) 264
General purpose tracking: fundamental research & applications
Motivation:
use PCB technology for mass production,
no floating structure
Spark-tolerant structure

## Slide 32: New gaseous neutron detectors
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
NMX Spectrometer @ ESS
B(Gd)-GEM & uTPC concept
GEM
GEM
GEM
Triple GEM + 3D borated cathode
Thermal neutrons
BANDGEM Modules
As rear detector panels
LOKI-SANS Instrument @ ESS

## Slide 33: Gaseous Photon Detectors
Particle Identification Techniques:
p (GeV/c)
p-K identification range
TR+dE/dx
Cherenkov
dE/dx
TOF
150 ps
FWHM
electron identification
need for π-K identification from HEP Experiments
- Large momentum acceptance  Cherenkov angle measurement technique
Large angular acceptance  large area of efficient single photon detection
1970s: large area position sensitive gaseous detectors available
Suitable photo-ionizing agent:
benzene: Seguinot-Ypsilantis NIM 142 (1977) 377,
TEA (7.6 eV) NIM 173 (1980) 283,
TMAE (5.3 eV) NIM 178 (1980) 125.
a gas gain high enough to detect single photoelectrons
conflicting requirements because of the copious UV emission by the multiplication avalanche.
solution: multistep avalanche chamber
(Charpak-Sauli Phys. Lett. B 142 (1977) 377) or TPC
Gaseous detectors: 1) cheap, 2) magnetic insensitive, 3) low material budget
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 34
OMEGA
DELPHI
TMAE(Tetrakis-Dimethylamine-Ethylene)
SLD - CRID
TEA (Tri-Ethyl-Amine)
CLEO III
E605
RICH with large area gaseous PD’s
1st generation: photoconverting vapours
Cherenkov photon
photoelectron
E
Townsend
avalanche
anode wires cathode pads
NIMA 554 (2005) 147
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 35: Thin CsI film
1956:
CsI layer has large QE for photons with hν > 6 eV
(Philipp and Taft)
CsI is highly reactive with water: it took many years to develop appropriate substrate preparation, deposition method, handling technology for high QE gaseous PDs
Cherenkov
photon
Townsend
avalanche
thin layer (300 - 500 nm) of
CsI on a cathode pad plane
Semitransparent photocathode:
thin metallic film and precise thickness.
Reflective photocathode:
no metallic film and non critical thickness
(important for large area)
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 36
RD26: the technology of MWPCs + CsI
François Piuz
1992, F. Piuz et al. Development of large area advanced fast-RICH detector for particle identification at LHC operated with heavy ions
  TO ACHIEVE HIGH CsI QE:
  Substrate preparation:
  Cu clad PCB coated by Ni (7 µm) and Au(0.5 µm), surface cleaning in ultrasonic bath, outgassing at 60 oC for 1 day
  Slow deposition of 300 nm CsI film:
  1 nm/s (by thermal evaporation or e--gun) at a vacuum
  of ~ 10-7 mbar, monitoring of residual gas composition
  Thermal treatment:
  after deposition at 60 oC for 8 h
  Careful Handling:
  measurement of PC response, encapsulation under dry Ar, mounting by glove-box.
The best fused silica cuts here
A. Di Mauro, NIM A 525 (2004) 173.
Schematic structure of the COMPASS Photon Detector:
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 37
MWPCs with solid state photocathode (the RD26 effort)
TIC, NA44
COMPASS RICH-1 2002 CsI > 5 m2
JLAB-HALL A
ALICE-HMPID
2009
CsI > 10 m2
STAR
HADES 1999
CsI > 1 m2
RICH with large area gaseous PD’s
2 nd generation: MWPC’s + CsI
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 38: MWPC’s with
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 39: CsI coated photocathodes
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 40: MWPCs with CsI: the limits
Severe recovery time (~ 1 d) after detector trips
  Ion accumulation at the photocathode moderate gain:<105
Feedback pulses (effective gain: <1/2)
  Ion and photons feedback from the multiplication process not fast
Aging after integrating a few mC / cm2
  Ion bombardment of the photocathode
H. Hoedlmoser et al., NIM A 574 (2007) 28.
1 mC/cm2
0.2 mC/cm2
MWPCs  slow signal formation
  + low gain  “slow” electronics (signal
  integration, low noise level)
  Gassiplex FE : integration time ~ 0.5 ms, time res> 1 ms
  APV (COMPASS RICH-1 upgrade) : resolution ~ 400 ns
   Detector memory, i.e. not adequate for high rates
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 41: MPGD-BASED PDs
Reduced photon feed-back and Ion BackFlow (IBF)
  Reduced ageing
  High gain  high photoelectron detection efficiency
Intrinsically fast gaseous detectors
Short integration time
  High rate environments
MICROPATTERN GASEOUS DETECTORS
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 42: ION & PHOTON BLOCKING GEOMETRIES
GEM-based PDs
A. Breskin and R. Chechik, NIM A 595 (2008) 116
Semi-transparent PC
Reflective PC
e- avalanche
ion avalanche
NO photon feedback
Reduced ion feedback
An “old” idea
R. Chechik et al., NIM A 419 (1998) 423
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 43: HBD – the basic concept
Proximity focus configuration, no window,
no mirror
CF4 radiator and active gas. Lrad=50 cm
Very large bandwidth
108 – 200 nm
(6.2 - 11.5 eV)
triple GEMs for
signal
multiplication
CsI photocathode
W. Anderson et al.,
NIM A 646 (2011) 35
0.65 m
Cherenkov
blobs
e+
e-
qpair
opening angle
B≈0
1.21 m
HBD- Cherenkov detector with GEMs +CsI
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Notes: The HBD is a windowless Cherenkov detector
CF4 radiator gas and active gas. Lrad=50 cm. Cherenkov threshold for pions 4 GeV/c
triple GEMs for signal multiplication
CsI photocathode evaporated on top of the triple GEM stack
proximity focused configuration – no mirrors, the Cherenkov light forms a circular blob image
hexagonal pad readout, with pad side = 1.55 cm
total weight per arm < 10 kg
total radiation length: 4.4%
0.9% (vessel) + 0.5% (CF4) + 3% (backplane)
Materials used:

## Slide 44
Electron signals are relatively rare (compared to hadrons)
Detector operated in reverse bias mode to repel the ionization charge from dE/dx
Cherenkov light is formed only by e+ or e-
Successfull operation at PHENIX since seversl years
It is not a detector of single photons
CsI (350 nm)
primary ionization from dE/dx
El. Field
photo
electron
mesh
GEMs
pads
HBD – hadron blindness
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
Notes: In order to enable measurement of relatively weak and rare electron signals in the overwhelming hadron environment, the following concept of hadron blindness has been developed:
Cherenkov light is formed only by e+ or e-, threshold for pi0 is 4 GeV/c
the detector is operated in reverse bias mode in which a reverse voltage is applied between the first GEM and a mesh to repulse the ionization charge coming from dE/dx
any remaining signals from hadron dE/dx will form a single pad blob in HBD, while single electrons will form a blob with an average of 3 pads
Reflective photocathode scheme:
photoelectrons are pulled into the holes by strong electric field
the photocathode is screened from avalanche photons

## Slide 45: OVERCOMING IBF
More complex geometries needed with extra electrodes to trap the ions:
Micro-Hole & Strip Plate (MHSP), COBRA
J.F.C.A. Veloso et al.,
Rev.Sc. Instr. 71 (2000) 2371
A.V. Lyashenko et al.,
JINST 2 (2007) P08004
MHSP
COBRA
A.V. Lyashenko et al.,
NIMA 598 (2009) 116
A.V. Lyashenko et al.,
NIMA 598 (2009) 116
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 46: THGEM-based PDs
PCB technology, thus:
robust
mechanically self supporting
industrial production of large size
boards
large gains have been immediately
reported (rim !)
Comparing to GEMs
Geometrical dimensions X ~10
  But e- motion/multiplic. properties do not!
  Larger holes:
    dipole fields and external fields
    are strongly coupled
    e- dispersion plays a minor role
introduced in // by different groups:
L. Periale et al., NIM A478 (2002) 377.
P. Jeanneret, PhD thesis, Neuchatel U., 2001.
P.S. Barbeau et al, IEEE NS50 (2003) 1285
R. Chechik et al, .NIMA 535 (2004) 303
RIM
About PCB geometrical dimensions:
Hole diameter : 0.2 – 1 mm
Pitch : 0.5 – 5 mm
Thickness : 0.2 – 3 mm
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 47: THGEM rate capability and IBF
High rate device
Irradiation:
8.9 KeV X-ray
0 20 40 60 80 100 120
Rate (kHz / mm2)
I (pA)
0 1000 2000
IBF control
single THGEM, no RIM
M. Alexeev et al., JINST 7 (2012) C002014
Triple THGEM:
Ion Back Flow
reduction by
staggering plates
IBFR (%)
A
ETR2 (kV/cm)
M
ETR2 (kV/cm)
ETR1 (kV/cm)
IBFR < 5% !
M. Alexeev et al. JINST 10 (2015 ) P03026
The gain in Thick GEM multipliers and its time-evolution
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 48: THGEM R&D for RICHes
ALICE VHMPID
THGEM & HYBRID
beam
Č photon
V.Peskov et al., NIMA 695 (2012) 154
COMPASS, RICH-1 upgrade by Triple THGEM detectors
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 49: HYBRID MPGD PDs (THGEM + MM)
Gain ~ 130K
Single Photon spectrum in BEAM !!!
The 1st THGEM forms the PC
The 2nd THGEM (staggered) forces the electron diffusion
The MM provides large gain, made larger by the diffusing the impinging electron cloud
THGEM
staggered !
beam
Č photon
The same architecture independently studied in parallel as GPM for DM searches (see later)
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 50
  stripping dry-film
  development
  etching
  image transfer
  multi-spindle drilling
  mounting
A post production specific surface treating and cleaning procedure developed in Trieste is applied:
Surface Polishing.
High pressure water cleaning.
Ultrasonic Bath with Sonica PCB solution (PH11), distilled water rinsing and oven @ 160 ºC
  drilling
THGEM production @ ELTOS and the surface treatment in Trieste
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 51
Mounting the detectors on the COMPASS RICH-1
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 52: First large area THGEM-based PDs
COMPASS RICH UPGRADE
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
TAKING DATA DURING 2016 RUN

## Slide 53
100 250 400 550 700 1100 1200
l (nm)
12.3 4.9 3.1 2.24 1.76 1.12 1.03
E (eV)
Different photocathodes and their thresholds
visible infrared
ultraviolet
TEA
TMAE,CsI
bialkali K2CsSb
Multialkali
NaKCsSb
GaAs
Si
external photoeffect
eQ < 50%
internal or external photoeffect
eQ > 50%
gas
vacuum
solid state
eQ = Q.E. = Ne / Ng
Photon detection involves often materials like K, Na, Rb, Cs (alkali metals). They have the smallest electronegativity  highest tendency to release electrons.
Most photocathodes are VERY reactive; Exceptions: Si and CsI.
Bled, 10/6/2015, 9th International Workshop on Ring Imaging Cherenkov Detectors RICH2016 - Fulvio Tessarotto

## Slide 54: PHOTOCATHODES FOR VISIBLE LIGHT
  Chemical reactivity (gas purity better than ppm level needed 
  UHV materials and sealed detectors)
  PC stability under ion bombardment - work function lower than CsI one
  AGEING CsI: -16% QE at 25mC/mm2
  Bilkaly: -20% QE at 0.4mC/mm2
A.V.Lyashenko et al., 2009 JINST 4 P07005
F-R-MHSP,
IBF: 3 x 10 -4
K-Cs-Sb vs CsI
T.Moriya et al., NIMA 732 (2013) 263
F.Tokanai et al., NIMA 628 (2011) 190
Doulble GEM,
IBF: ~ 10 -2
F. Tokanai et al., NIMA 610 (2009) 164
Bialkali,
Gas P 675 torr
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 55: GASEOUS DETECTORS FOR VISIBLE LIGHT
the GEM approach
Pulsed ion gating
Breskin et al.,
NIMA 553 (2005) 46
Multiple GEM
sealed
K-Cs-Sb - Continuous
mode, not a sealed PD
A.V.Lyashenko et al.,
2009 JINST 4 P07005
R.Chechik
et al., NIMA
502 (2003) 195
Poor compatibility of bialkali and GEM material ?
Extremely poor QE of the bialkali PC:
the material of the GEM chemically reacts with the bialkali metals
F. Tokanai et al., NIMA 610 (2009) 164
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 56: GASEOUS DETECTORS FOR VISIBLE LIGHT
the Micromegas approach
K-Cs-Sb
Double MM, Ni mesh
Vacuum, 20%
Ar (90%)+CH4 (10%)
12% (stable) after 1.5 y
IBF : <2.5×10−3
Gain < 104
F. Tokanai et al., NIMA 610 (2009) 164
2 staggered MM layers to enhance ion trapping
In collaboration with HAMAMATSU
IBF : 6 ×10−4
Gain : 104
F. Tokanai et al., NIMA 766 (2014) 176
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 57: GASEOUS DETECTORS FOR VISIBLE LIGHT
H. Sugiyama et al., NIMA (2016) in press
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 58: Scintillating Glass-GEM imager
T. Fujiwara, et al., JINST 8 C12020, 2013
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 59: CRYOGENIC MPGD-PDs
Read-out elements of cryogenic noble liquid detectors
  Rear event detectors (n, DM)
  Detecting the scintillation light produced in the noble liquids
  Options of scintillator light and ionization charge detection by a same detector !
with WINDOW WINDOWLESS OPERATED IN THE
(2-PHASES) CRYOGENIC LIQUID
L.Arazi et al., JINST 8 (2013) C12004
S.Duval et al., JINST 6 (2011) P04007
Bondar et al.,NIMA 556 (2006) 273
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 60: Bubble-assisted electroluminescence in LXe
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 61: Dual-phase LAr LEM TPC
C.Cantini et al.,
JINST 10 P03017
(2015)
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 62: LARGE SIZE PROJECTS
LBNO – GLACIER (THGEM)
DUNE (40-kt LAr)
(THGEM)
(bulkMM)
Panda-X, THGEM +
MM (dark matter)
DARWIN
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto

## Slide 63: CONCLUSIONS
Moscow, 12/10/2016, 2nd International Conference on Particle Physics and Astrophysics ICPPA-2016 - Fulvio Tessarotto
THE DEVELOPMENT OF MPGDS IS SUCCESSFUL AND EXPANDING
  Consolidated technologies are spreading over small and large projects
  Advanced R&D is making continuous progress on new solutions
NEW GENERATION OF GASEOUS PHOTON DETECTORS
  Large size MPGD-based PDs operating in Experiment
  Progress toward gaseous visible light PD
BRIGHT FUTURE FOR:
  Inventions: new ideas, new techniques
  Technology consolidation, new applications
  Large scale projects