## Slide 1
Gamma-quanta and charged particles recognition by the counting and triggers signals formation system of GAMMA-400 space gamma-telescope
I.V. Arkhangelskaja1,
A.I. Arkhangelskiy1, E.N. Chasovikov1, M.D. Kheymits1,
Y.T. Yurkin1, A.M. Galper1,2, S.I. Suchkov2,
N.P. Topchiev2, A.E. Murchenko1
1National Research Nuclear University MEPhI
(Moscow Engineering Physics Institute)
2 Lebedev Physical Institute, Russian Academy of Sciences

## Slide 2
Main
Additional
lateral

## Slide 4
The main aperture |  |  |  |  |  |  |  |  | The additional aperture |  |  |  |  |  |  | The lateral aperture |  |  |  |  |  | 
 |  |  |  |  | е+/е_ |  | nuclei |  |  |  |  | е+/е_ |  | nuclei |  |  |  | е+/е_ |  | nuclei |  | 
 | Еlow1 | Еlow2 | Еm | Еh | Еm | Еh | Еm | Еh | Еlow | Еm | Еh | Еm | Еh | Еm | Еh | Еlow | Еh | Еm | Еh | Еm | Еh | 
АСtop (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
AClat (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LD system (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TOFsystem (signal TOF): the combination of S1 and S2 sections upper and lower layers individual detectors energy deposition with time-coordinate compensation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Signals BS1_ACtop (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system АСtop one |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Signal BS1_AClat (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system AClat one |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Signal BS1t (time analysis backsplash): the time delay between combination of both layers individual detectors of TOF S1 section and АСtop one |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Signal BS2 (amplitude backsplash): the combination of both layers individual detectors of TOF S2 section and LD one energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Signal BS3 (amplitude backsplash): the combination of both layers individual detectors of calorimeter scintillation detectors sections S3, S4 and anticoincidence detectors LD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Time of light system detector S1 energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Time of light system detector S2 energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 amplitude discriminators |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Strip detectors CC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S3 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S4 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 amplitude discriminators |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Strip detectors of converter C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Neutron detector |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
coincidence
anti-
coincidence
energy deposition
energy deposition
energy deposition
energy deposition
energy deposition
energy deposition

## Slide 6
Direct energy deposition in double layers ACtop for relativistic protons (grey) and electrons (black) used for thresholds definition.

## Slide 7
Direct energy deposition in double layers ACtop for 3 GeV protons used for thresholds definition.

## Slide 8
Direct energy deposition in double layers ACtop for 100 GeV γ-quanta with backsplash subtraction using temporal analysis (area marked (1) contains ~60% of events with energy deposition less than 1 keV in both ACtop layers)

## Slide 9
Direct energy deposition in double layers ACtop for 3 GeV γ-quanta with backsplash subtraction using temporal analysis (area marked (2) contains ~70% of events with energy deposition less than 1 keV in both ACtop layers)

## Slide 10
Triggers in the main aperture will be formed using information about particle direction provided by time of flight system and presence of charged particles or backsplash signal formed according to analysis of energy deposition in combination of both layers anticoincidence systems АСtop and AClat individual detectors.
For double-layer ACtop less than 3% photons will be wrongly recognized as electrons or protons for ~3-100 GeV particles. The part of charged particles mistakenly identified as gammas will be ~10-5 using described algorithms.

## Slide 11
Amount of particles with non-zero energy deposition in plastic detectors. |  |  |  |  | 
Detector layer | e- 1MeV | e- 3MeV | e- 10MeV | р 30 MeV | р 100 MeV
AC top upper level | 161 | 9834 | 9992 | 9936 | 9996
AC top lower layer | 75 | 401 | 9640 | 38 | 9936
S1 upper layer | 0 | 17 | 122 | 2 | 256
S1 lower layer | 1 | 16 | 123 | 0 | 225
S2 upper layer | 0 | 4 | 77 | 5 | 100
S2 lower layer | 0 | 11 | 75 | 3 | 85
S3 upper layer | 0 | 4 | 16 | 0 | 7
S3 lower layer | 0 | 1 | 12 | 0 | 3
Maximal energy deposition in plastic detectors, MeV. |  |  |  |  | 
Detector layer | e- 1MeV | e- 3MeV | e- 10MeV | р 30 MeV | р 100 MeV
AC top upper level | 0.199 | 2.668 | 9.343 | 20.983 | 96.570
AC top lower layer | 0.261 | 1.659 | 6.069 | 5.823 | 79.943
S1 upper layer | 0 | 0.766 | 3.371 | 1.364 | 17.906
S1 lower layer | 0.450 | 0.875 | 3.948 | 0 | 21.944
S2 upper layer | 0 | 0.322 | 2.831 | 0.467 | 13.779
S2 lower layer | 0 | 0.320 | 1.926 | 0.975 | 2.468
S3 upper layer | 0 | 0.255 | 0.904 | 0 | 1.225
S3 lower layer | 0 | 0.041 | 0.705 | 0 | 0.021
Low energy charged particles

## Slide 12
Fragment of sample 3 MeV electron full tracking |  |  |  |  |  |  |  |  | 
Detector layer | Particle type | Par-ticle ID | Parent ID | Process | E, MeV | Etotal, MeV | X, mm | Y, mm | Z, mm
T.i. upper foil T.i. polyamide | e- | 1 | - | bremsstrahlung bremsstrahlung | 0.654 0.314 | 2.346 2.032 | 376.33 376.32 | 200.17 200.16 | -1309.92 -1309.47
T.i. lower foil | e- | 1 | - | Transportation | 0.050 | 1.981 | 376.31 | 200.17 | -1309.30
AC top upper | e- | 1 | - | Multiple scattering | 0.144 | 1.402 | 379.14 | 197.72 | -1253.09
AC top upper | e- | 1 | - | Multiple scattering | 0.202 | 1.200 | 379.24 | 196.91 | -1252.94
AC top upper | e- | 1 | - | Multiple scattering | 0.213 | 0.987 | 379.46 | 196.104 | -1252.98
AC top upper | e- | 1 | - | Multiple scattering | 0.188 | 0.780 | 380.06 | 195.64 | -1252.92
AC top upper | e- | 1 | - | Ionisation | 0.289 | 0.511 | 380.32 | 195.44 | -1252.62
T.i. lower foil layer |  | 2 | 1 | Transportation | 0 | 1.165 | 376.37 | 200.15 | -1309.30
AC top upper |  | 2 | 1 | Transportation | 0 | 1.165 | 400.73 | 197.09 | -1233.80
AC top lower |  | 2 | 1 | Transportation | 0 | 1.165 | 407.18 | 196.28 | -1213.80
Converter |  | 2 | 1 | Transportation | 0 | 1.165 | 444.60 | 191.56 | -1097.80
S1 upper |  | 2 | 1 | Transportation | 0 | 1.165 | 449.78 | 190.92 | -1081.80
S1 lower layer |  | 2 | 1 | Transportation | 0 | 1.165 | 452.99 | 190.51 | -1071.80
S2 upper |  | 2 | 1 | Transportation | 0 | 1.165 | 629.26 | 168.32 | -525.40
S2 lower |  | 2 | 1 | Compton | 0.266 | 0.899 | 631.56 | 168.03 | -518.27
S2 lower layer |  | 2 | 1 | Transportation | 0 | 0.899 | 632.72 | 166.14 | -515.40
CC1 upper l |  | 2 | 1 | Transportation | 0 | 0.899 | 679.19 | 90.11 | -400.00
CC1 lower |  | 2 | 1 | Transportation | 0 | 0.899 | 724.00 | 16.82 | -288.75
CC1 lower |  | 2 | 1 | Compton | 0.204 | 0.695 | 726.57 | 12.61 | -282.36
CC1 lower |  | 2 | 1 | Transportation | 0 | 0.695 | 726.37 | 12.24 | -280.00

## Slide 13
The additional aperture |  |  |  |  |  |  |  | 
 |  |  |  | е+/е_ |  | nuclei |  | 
 | Еlow | Еm | Еh | Еm | Еh | Еm | Еh | 
АСtop (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  | 
AClat (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  |  | 
LD system (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  |  | 
TOFsystem (signal TOF): the combination of S1 and S2 sections upper and lower layers individual detectors energy deposition with time-coordinate compensation |  |  |  |  |  |  |  | 
Signals BS1_ACtop (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system АСtop one |  |  |  |  |  |  |  | 
Signal BS1_AClat (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system AClat one |  |  |  |  |  |  |  | 
Signal BS1t (time analysis backsplash): the time delay between combination of both layers individual detectors of TOF S1 section and АСtop one |  |  |  |  |  |  |  | 
Signal BS2 (amplitude backsplash): the combination of both layers individual detectors of TOF S2 section and LD one energy deposition |  |  |  |  |  |  |  | 
Signal BS3 (amplitude backsplash): the combination of both layers individual detectors of calorimeter scintillation detectors sections S3, S4 and anticoincidence detectors LD |  |  |  |  |  |  |  | 
Time of light system detector S1 energy deposition |  |  |  |  |  |  |  | 
Time of light system detector S2 energy deposition |  |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 amplitude discriminators |  |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 |  |  |  |  |  |  |  | 
Strip detectors CC1 |  |  |  |  |  |  |  | 
S3 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  | 
S4 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 amplitude discriminators |  |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 |  |  |  |  |  |  |  | 
Strip detectors of converter C |  |  |  |  |  |  |  | 
Neutron detector |  |  |  |  |  |  |  | 
energy deposition
energy deposition
energy deposition

## Slide 15
The lateral aperture | The lateral aperture |  |  |  |  |  | 
 |  |  | е+/е_ |  | nuclei |  | 
 | Еlow | Еh | Еm | Еh | Еm | Еh | 
АСtop (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  | 
AClat (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  | 
LD system (outer and inner layers individual detectors) energy deposition |  |  |  |  |  |  | 
TOFsystem (signal TOF): the combination of S1 and S2 sections upper and lower layers individual detectors energy deposition with time-coordinate compensation |  |  |  |  |  |  | 
Signals BS1_ACtop (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system АСtop one |  |  |  |  |  |  | 
Signal BS1_AClat (amplitude backsplash analysis): the combination of both layers individual detectors energy deposition of TOF S1 section and anticoincidence system AClat one |  |  |  |  |  |  | 
Signal BS1t (time analysis backsplash): the time delay between combination of both layers individual detectors of TOF S1 section and АСtop one |  |  |  |  |  |  | 
Signal BS2 (amplitude backsplash): the combination of both layers individual detectors of TOF S2 section and LD one energy deposition |  |  |  |  |  |  | 
Signal BS3 (amplitude backsplash): the combination of both layers individual detectors of calorimeter scintillation detectors sections S3, S4 and anticoincidence detectors LD |  |  |  |  |  |  | 
Time of light system detector S1 energy deposition |  |  |  |  |  |  | 
Time of light system detector S2 energy deposition |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 amplitude discriminators |  |  |  |  |  |  | 
Individual scintillation detectors of CC1 |  |  |  |  |  |  | 
Strip detectors CC1 |  |  |  |  |  |  | 
S3 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  | 
S4 (upper and lower layers individual detectors) energy deposition |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 amplitude discriminators |  |  |  |  |  |  | 
Individual scintillation detectors of СС2 |  |  |  |  |  |  | 
Strip detectors of converter C |  |  |  |  |  |  | 
Neutron detector |  |  |  |  |  |  | 
energy deposition

## Slide 17
Conclusions:
to provide particles registration and recognition in the main aperture :
  At least 2 layers of plastics in AC (both top and lateral)
  At least 20% energy deposition in plastics
  At least 2 layers of scintillators in CC1
  S3 between CC1 and CC2
  Several discriminators in plastics and CC1 to provide different thresholds of energy deposition fast analysis
+ For additional aperture:
1) At least 2 layers of plastics in LD
2) At least 2 layers of plastics in S4 and several
discriminators in S4
+ for lateral aperture: several discriminators in CC2

## Slide 18
Energy band | Energy resolution
0.1-0.25 GeV | from ~30% up to ~15%
0.25 – 1 GeV | from ~15% up to ~9%
1 – 10 GeV | from ~9% up to ~2.7%
10-102 GeV | from ~2.7% up to 2%
> 102 GeV | 2%
the main aperture
Aperture type | Energy band | Energy resolution
Additional | 1-10 MeV | from 3% up to 2%
 | 10-102 MeV | 2%
 | 0.1-1 GeV | 2%
 | > 1 GeV | 2%
Lateral | 0.2-1 MeV | from ~9% up to ~3%
 | 1-5 MeV | ~3%
 | > 10 MeV | ~2%

## Slide 19
Thank you for attention!!!!!