## Slide 1: Physics program of the NICA facility at JINR
V. Kekelidze,
JINR, Dubna
NICA
Volga
river
II ICPPA, October 10 - 14, 2016, Moscow
Notes: Dear members of Scientific Committee let me give a brief presentation on the status of NICA project

## Slide 2
NICA (Nuclotron based Ion Colider fAcility)
Main targets:
- study of hot and dense baryonic matter
at the energy range of max baryonic density
- investigation of nucleon spin structure, polarization phenomena
- development of accelerator facility for HEP @ JINR
construction of Collider of relativistic ions from p to Au,
polarized protons and deuterons
with max energy up to √SNN= 11 GeV (Au79+) and =27 GeV (p)
Ione source
Notes: Main targets of the project are: ; that requires a development …

## Slide 3
Injection Complex
Booster
Nuclotron
Collider
Cryogenic Complex
Detector BM@N
MPD
SPD
Magnet production line
Computing
Infrastructure
major blocks of the NICA
Notes: There are 10 major blocks of the NICA project

## Slide 4
  Machine Advisory Committee:
  Boris Sharkov, ITEP, chairman
  Pavel Beloshitsky, CERN
  Sergei Ivanov, IHEP
  Thomas Roser, BNL
  Alexei Fedotov , BNL
  Markus Steck, GSI
  Nicholas Walker, Desy
  Sergei Nagaitsev, FNAL
Accelerator blocks
  Alexander Zlobin, FNAL
  Takeshi Katayama, Tokyo Univ.
  Valeri Lebedev, FNAL
  Rolf Stassen, FZJ
  Yuri Senichev, FZJ
  Evgeny Levichev, BINP
  Victor Yarba, FNAL
  Pavel Zenkevich, ITEP
Leaders:
G. Trubnikov, I. Meshkov, A. Butenko, A. Kovalenko
The TDR is approved
Notes: The accelerator blocks were comprehensively revised by the MAC. The TDR is approved.

## Slide 5
New fore-injector for LU-20 + SPI
A.Butenko,
A.Govorov,
V.Monchinsky,
T.Kulevoy,
S.Polozov
V.V.Fimushkin
A.S.Belov
…
16 of May – beam accelerated in LU-20
12 of June - the deuteron beam from
SPI accelerated in the Nuclotron ring
COMMISSIONED
RUN #52, d+
Energy 750 MeV/u, intensity 109

## Slide 6
RFQ
IH-1
IH-2
MEBT
COMMISSIONED
MOUNTED
COMMISSIONED
MOUNTED
Heavy Ion Linear Accelerator HILAc
overall commissioning: Oct. 16

## Slide 7
SC Magnets for Booster, Collider & SIS-100/FAIR
workshop at VBLHEP JINR (bld. 217)
Serial tests of Booster magnets has started
procurement of magnet systems is in progress
status of yoke proc. 06.09.2016 |  |  | 
 | total | schedule | delivered yokes
dipoles | 40 | 40 | 21
quadrupoles | 48 | 48 | 42

## Slide 8
cooling
preparation
repairing
accelerator physics
and R&D of user
Technical Run 52 of the Nuclotron (d , d)
(02.06 – 08.07.2016)
5 experiments at extracted beams:
1 experiments with polarized beam (data taking);
4 experiments with unpolarized beams (R&D and calibrations ).
 456 hours scheduled for users.
 120 hourst obtained
SPI (unpolarized mode)RFQ LU-20 Nuclotron OK!
Polarimeters (the Low Energy Polarimeter (after LU-20) and the ITS
polarimeter at the internal beam) were prepared for measurements.
SPI (vector polarized mode) + LEP  OK (16.06.16 - 7.07.16):
vector polarization – as expected  (+/- 0.5)
time distribution

## Slide 9
The whole Complex comprises several Objects to be commissioned:
MPD Hall, I q., 2018
SPD Hall, II q., 2019
West semi-ring,
III q., 2018
East semi-ring,
IV q., 2018
Beam transport ch.,
I q., 2019
Bld.#1reconstruction,
I q., 2019
Civil Construction of NICA Complex
STRABAG – General contractor; КометА – designer
The works are in progress: piling, subcontractor for iron/concrete works

## Slide 10
the construction is in progress

## Slide 11
MultiPurpose Detector (MPD)
Baryonic Matter at Nuclotron (BM@N)
the fixed target experiment
at the Nuclotron
at the Collider
SPD (Spin Physics Detector) at the Collider
the project - in preparation
3 detectors
Stage I 2017
Stage I 2020
Notes: 3 detectors will be constructed: one for the fixed target experiment and two at the collider. The project for SPD detector is in preparation.

## Slide 12
 | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  | 
Injection complex |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lu-20 upgrade |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Source |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Linac |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nuclotron |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
general development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
extracted channels |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
startup configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
design configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BM@N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
II stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
solenoid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TPC, TOF, Ecal (barrel) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
upgraded end-caps |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Civil engineering |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
collider tunnel |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HEBT Nuclotron-collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NICA schedule
running time

## Slide 13
NICA program in heavy ion collisions
and
experimental strategy
for 2020-2023

## Slide 14
Exploration of the QCD Phase Diagram
NICA
Exploring high-density baryonic matter: maximun freeze-out density
Jurgen Randrup, Jean Cleymans
NICA is well suited for exploring the transition between the hadronic phase and the new plasma phase. This exploration is the top priority of the NICA program

## Slide 15
STAR F.T.
HADES
CBM
Interaction rate [Hz]
Collision energy √S [GeV]
NN
NICA/BM@N II
Present and future HI experiments
NA-61/SHINE
2022 – 2025: SIS-100 FAIR
energy region of max.
baryonic density
NICA/MPD
STAR BES II
Notes: Concerning fixed target experiments –there are several ones including NICA/BMN. CBM/FAIR will provide extremely high interaction rate.

## Slide 16
Both, collider and fixed target approaches,
are complementary and necessary
for approval of potential discovery
In this view the NICA and FAIR projects are complementary
and their joined efforts have aimed to
discovering and to studying new forms of baryonic matter

## Slide 17
STAR F.T.
HADES
CBM
Interaction rate [Hz]
Collision energy √S [GeV]
NN
NICA/BM@N II
Present and future HI F.T. experiments
NA-61/SHINE
2022 – 2025: SIS-100 FAIR
energy region of max.
baryonic density
Notes: Concerning fixed target experiments –there are several ones including NICA/BMN. CBM/FAIR will provide extremely high interaction rate.

## Slide 18
Baryonic Matter at Nuclotron (BM@N)
Detector Advisory Committee:
Hans Rudolf Schmidt, Tubingen Uni. - chairman
Hans Gutbrod, GSI
Itzhak Tserruya, Weitzmann Istitute
Peter Hristov, CERN
Karlheinz Hiller, DESY
Leader: M. Kapishin
Notes: This detector will operate at the beam extracted from the Nuclotron.

## Slide 19
BM@N: the 1st stage
area prepared for detector installation
Participants from:
Russia: INR, MEPhi, SINP, MSU,
IHEP, S-Ptr Radium Inst.
Bulgaria: Plovdiv University;
China: Tsinghua University, Beijin;
Poland: Warsaw Tech.Uni.
Israel: Tel Aviv Uni.
Germany: Frankfurt Uni.
+ expression of interest from CBM
Physics:
strange / multi-strange hyperon and hypernuclei production
at the threshold
hadron femtoscopy
event-by event fluctuations
in-medium modifications of strange & vector mesons
in dense nuclear matter
electromagnetic probes, states decaying into γ, e (with ECAL)
Notes: The participants from several institutions are contributing to the experiment preparation. At the fist stage it will be studied: strange and …..

## Slide 20
area prepared for detector installation
BM@N status and milestones
BM@N schematic view
BM@N configuration
DAQ GEM (CERN) ST TOF Outer tracker
2016, IV: basic 6 half 1 small half DCH
        config. planes plane config.
2017, III: complete 10 h/pl. 2 s/pl. basic DCH
2019, I: -”- 8-10 full pl. 2 s.,2 large pl. complete Straw+DCH
Notes: Several milestones are foreseen to put in operation the fully equipped detector. There major tracker is based on the GEM detectors fabricated with the help of CERN.
Silicon tracer is produced in cooperation with the GSI and other institutions.

## Slide 21
d beam (~5·105 /cycle) with 2.94 GeV/n
5 GEM detectors 66 x 41cm2 + 1 detector 163 x 45 cm2
BM@N Run 52 (June 2016): tests & commissioning
of GEM CT located inside analyzing magnet

## Slide 22
GEM detectors for central tracker
Tests of GEM detector 163 x 45 cm2
Set of 5 GEM detectors 66 x 41 cm2 prepared for cosmic tests, June 2016
GEM design and production at CERN workshop is going slower
than expected
5 detectors 66 x 41 cm2 and 2 detectors 163 x 45 cm2 are foreseen to use
in technical run at the end 2016
6-8 more detectors 163 x 45 cm2 should be commissioned in autumn 2017 plan to produce

## Slide 23
beam
Performance of GEM tracker in séance 52, June 2016
5 middle size + 1 big GEM detectors
Products of interaction with target & proton spectators / pile-up events in center
Beam spot
(detectors are displaced to ±15 mm)
beam profile
in middle GEM detector
beam track residuals in big GEM detector

## Slide 24
BM@N feasibility study
area prepared for detector installation
ToF-700
Scint-700
DCH-1,2
ZDC
3HΛ → 3He π-
Ξ-
2,6M central events
8,5M 3HΛ in 1 m, 20 kHz trigger
A.Zinchenko, V.Vasendina
Simulation: UrQMD & DCM-QGSM, Au+Au 4,5 AGeV
900 k central events
7,5M X- in 1 m, 20 kHz trigger
Notes: The second technical run is foreseen in May-june. The first physics run is planned at the end of 2017 when the Booster will be put in operation. The run with high intensity gold beam is planned in 2019. The simulation indicates a reliable detection of cascades and hyper-nuclei.

## Slide 25
year | 2016 | 2017 spring | 2017 autumn | 2019 | 2020 + ..
beam | d ( ) | C, Ar | Kr | Au | Au, p
maximum intensity, Hz | 1M | 1M | 1M | 1M | 10M
trig. rate, Hz | 10k | 10k | 20k | 20k | 50k
central tracker | 6 GEM half pl. | 8 GEM half pl. | 10 GEM half pl. | 8 GEM full pl. | 12 GEM or 8+2Si
expiment status | techn. run | techn. run | physics run | physics stage 1 | physics stage 2
BM@N plans

## Slide 26
MultiPurpose Detector (MPD)
Detector Advisory Committee:
Hans Gutbrod, GSI - chairman
Itzhak Tserruya, Weizmann Institute
Hans Rudolf Scmidt, Tubingen Uni.
Jean Cleymans, Cape Town Uni.
Nu Xu, BNL
Coordinator: V. Golovatyuk
TDRs for most sub-detectors have been prepared
and now are under evaluation by DAC
Notes: The MPD will be the fist detector operated at the Collider. The TDRs for…

## Slide 27
NICA/MPD
STAR BES II
Interaction rate [Hz]
Collision energy √S [GeV]
NN
Present and future HI collider experiments
energy region of max.
baryonic density
Notes: Only two collider experiments can explore the energy range of maximum baryonic density: Beam energy scan of STAR and NICA/MPD.
However at different interaction rates.

## Slide 28
MPD experimental strategy
Bulk observables (hadrons): spectra,yields (OD, EOS) from p to W
(charm is under evaluation)
Event-by-event fluctuation in hadron productions (CEP)
Femtoscopy: correlations involving p, K, p, L … (OD)
Directed & elliptic flows for identified hadron species (EOS,OD)
Multi-strange hyperon production : yields & spectra (OD, EOS)
Electromagnetic probes (CSR, OD) – limited specifications in 2019
Hypernuclei
OD – Onset of Deconfinement CEP – Critical End Point
CSR – Chiral Symmetry Restoration EOS – Equation Of State
measure a variety of observables systematically changing
collision conditions: energy, centrality, system size;
reference data (i.e. p+p) will be taken at the same conditions
Observables:
Notes: 28

## Slide 29
NICA parameters at very beginning (from 2020)
Start-up version (2020)
reduced luminosity: 5 .1025 at 11 GeV/A
enlarged beam diamond: s =0.6 m
This is the goal for 2023!

## Slide 30
FFD
MPD detector for Heavy-Ion Collisions @ NICA
Tracking: up to |h|<1.8 (TPC)
PID: hadrons, e, g (TOF, TPC, ECAL)
Event characterization:
centrality & event plane (ZDC)
Stage 1: TPC, TOF, ECAL, ZDC, FD
Status: technical design and detector R&D – completed;
Preparation for the mass production
Stage 2: IT + Endcaps (tracker, TOF, ECAL)
Notes: The MPD will be put in operation at two stages. At the first one the barrel part will be equipped with major tracking detector TPC, TOF end ECAL. ZDC and FD will be in operation as well.
At the second stage the detector will be supplemented with IT and end cap subdetectors.

## Slide 31
strategy in 2020-2023
energy and system size scan from 4 to 11 GeV in steps of 1-2 GeV
limitation by the accelerator:
lower luminosity
extra reduction by 40% because of a larger beam diamond
Detector limitation
TPC tracking: |h|<1.8 (N points>10)
TOF coverage: |h|<1.2
PID: combined |h|<1.2, 0.1<pT<4 GeV/c,
limited in 1.2 < |h|>1.8 (only dE/dx)
ECAL coverage : |h|<2.5
FHCAL coverage: 2.2<|h|<4.8
FD inside the TPC inner pipe

## Slide 32
Acceptance on h
MEPhI: P. Parfenov, I. Svintsov, I. Selyuzhenkov, A. Taranenko

## Slide 33
data rates
Beam | Luminosity (cm -2 c - 1) |  | Data sample per 1 week at √s = 4 GeV | Data sample per 1 week at √s = 11 GeV
 | √s=4 GeV | √s=11 GeV |  | 
197Au | 7 .1024 | 5 . 1025 | 9.1 . 106 | 6.3 . 107
possible scenario:
to take data at 8 energies 4, 5, 6, 7, 8, 9, 10, 11 GeV
for beam/target combinations: Au+Au, Xe+Xe, C+C, p+p
In total: 32 data sets (1 week for each of the top-half energies
and 2 weeks for lower energies).
In 48 weeks (~1,5 year) of data taking the statistics equal to one
at RHIC will be accumulated (duty factor 0.5 is used)

## Slide 34
Particle yields in Au+Au collisions @ √sNN = 8 GeV
(central collisions)
one week of running at L = 5 1025cm-2s-1 (duty factor = 0,5)
Particle | Multiplicity | Decay mode | BR | *Efficiency % | Yield /1 w
p+ | 293 | ---- | --- | 61 | 7.7 . 108
K+ | 59 | --- | ---- | 50 | 1.5 . 108
p | 140 | --- | ---- | 60 | 4.2 . 108
L | ~35 | p+p- | 64% | ~10% | ~1 . 107
X - | ~2 | L+p- | ~100% | 1.6% | 1.0 . 105
r | 31 | e+e- | 4.7 . 10-5 | 35 | 2.5 . 103
w | 20 | e+e- | 7.1 . 10-5 | 35 | 2.5 . 103
j | 2.6 | e+e- | 3 . 10-4 | 5 | 2.0 . 102
W | 0.14 | L+K | 0.68 | 2 | 9.5 . 103

## Slide 35
Good probes to indicate medium modifications of spectral functions due to chiral symmetry restoration in A+A collisions; effect is proportional to baryon density
σω≈14 MeV/c2
MPD performance for dileptons
Hadron suppression
up to 10-5
meson | Yields |  | Yield/1 w
 | 4p | y=0 | 
r | 31 | 17 | 7 . 104
w | 20 | 11 | 7 . 104
j | 2.6 | 1.2 | 1.7 . 104
Yields, central Au+Au st √sNN = 8.8 GeV/u
PID
Zinchenko, at SQM-2015

## Slide 36
~ 106 3ΛH are expected
in 10 weeks
P = 1 GeV/c
d
3He
p
p-
3ΛH → 3He + π –
PID
3ΛH → p + d + π -
Hypernuclei @ MPD
Hypertritons (central Au+Au @ 5A GeV (DCM-QGSM)
Hypernuclei production
enhanced at high
baryon densities (NICA)
M. Ilieva, at “SQM-2015”

## Slide 37
Early study from V. Kireev
at √s=4 GeV MPD accumulates ~100 PIDed protons (73%),
efficiency drops to 55% at ZVertex=120cm
MPD perspectives for ev-by-ev fluctuations at Stage’1
Central Au+Au.
15
Defined by the phase-space (barrel), PID performance
and (partially) by beam dimensions
Maximal allowed phase-space
even for a limited set of MPD elements

## Slide 38
primary vertex reconstruction with
TPC tracks: sZ ~ 200 mm is stable
within |Z|<100 cm
MPD perspectives for event-by-event fluctuations at Stage’1
Peripheral Au+Au √s=4 GeV
<Ntracks> ~ 50 (b=10 fm)
15
Is defined by the FHCAL performance, phase-space, tracking and PID performance, and (slightly) by beam dimensions
good v1,2 event plane resolution
using FHCAL

## Slide 39
O. Rogachevsky, A. Sorin, O. Teryaev,
Phys. Rev. C 82, 054910, 2010.
O.Teryaev, M.Baznat, K.Gudima, A.Sorin, XXIII Baldin Seminar,2016
M. Lisa, for the STAR collaboration,
SQM2016, Berkeley, June 2016
M. Baznat, K. Gudima, A. Sorin, O.Teryaev
Phys. Rev. C (2013); Phys. Rev C (2015);
A. Sorin, O. Teryaev arXiv:1606.08398
Spin effects in HI collisions
as a complementary probe

## Slide 40
Observable | Set-up | Coverage | New insights
Hadron yields & ratios | TPC, TOF, FHCAL,ECAL | ¦h¦ < 1.5 pT < 4 GeV/c | Data for 4<√s<7 GeV, critical assessment of y-spectra and K/p-ratio
Hyperons: yields, flow, Polarization | TPC, TOF FHCAL | ¦h¦ < 1.5 pT < 4 GeV/c | New data on yields, flow and polarization at √s < 7 GeV.
Dileptons | TPC, TOF ECAL, FHCAL | ¦h¦ < 1.2 pT < 3 GeV/c | low statistics data for comparison
Fluctuations & Correlations | TPC, TOF ECAL, FHCAL | ¦h¦< 1.5 | New data on Ev-by-Ev fluct. for √s > 4 GeV
Chiral Magnetic & vortical effects | TPC, TOF FHCAL | ¦h¦ < 1.5 pT < 3 GeV/c | Data @ √s < 7GeV (CME) Vortical @ 4 < √s < 11 GeV
(Hyper)Nuclei | TPC, TOF ZDC | ¦h¦ < 1.5 pT< 5 GeV/c | low statistics data for comparison
MPD physics cases (2020-2023)
In stage-II one should consider efficient measurements of open-charm hadrons, di-leptons, and direct photons.

## Slide 41
MPD status

## Slide 42
Control Dewar,
pipe lines
Cryostat
SC coil
Trim Coil
MPD superconducting Solenoid
ASG superconducting
(Genova, Italy):
Cold Mass + Cryostat
Vacuum System
Trim Coils
Control System
PS
General responsibility
TPC region
weight ~ 900 t
B0=0.66 T
Contract - signed; works – in progress
high level (~ 3x10-4) of magnetic
field homogeneity
Notes: The major part of MPD is SC solenoiodal magnet. It is a challenging project due to very high requirement for the magnetic field homogeneity – better that a permill.
After long negotiations a contract is signed with the ASG sc company – the one which produced a big solenoid for CMS. The ASG is responsible for production of coils, cryostat control system etc. In addition the company takes responsibility for the overall supervision and final characteristics.

## Slide 43
VITKOVICE Heavy Machinery, Sept. 5, 2016
Yoke production: all packages are at Vitkovice HM

## Slide 44
Schedule for MPD Magnet fabrication & commissioning
critical !
Of navigation in Volga. And water | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  |  | 2019 |  |  | 
 | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV
Contract with ASG |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- final design report | - |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- trim coils + forgings |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- SC cable, cryostat, coils |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- FAT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- delivery to Dubna |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- tests & overall commissioning |  |  | - |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Yoke production |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- contract preparation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- production drawings |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- production & assembly test |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- delivery to Dubna |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Preparatory works & cryo (ILK / JINR) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
System of movement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- technical design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- production and delivery to Dubna |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Assembly and tests (JINR / ASG) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
The field measurement (JINR /CERN) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Readiness for MPD integration |  |  |  |  |  |  |  | the MPD Hall is available |  |  |  |  |  |  |  |  |  |  |  | 
34 months
delivery by sea
Notes: A schedule for magnet fabrication and delivery is critical because of limitation of Volga navigation.

## Slide 45: Time Projection Chamber
TPC Prototype
Sketch of TPC
3400
Ø2800
12 Readout
chamber
beam
beam
HV-electrode
~ 28 kV
~ 110 000 readout channels
E
E
Project status:
basic R&D finished,
(cont. alternative RO Ch.);
assembly workshop
in preparation
(readiness – IIq., 2016)
C2
C3
Works are going in accordance with the schedule
Leaders: S. Movchan, Yu. Zanevsky

## Slide 46: Time Projection Chamber
Works are going in accordance with the schedule
Leaders: S. Movchan, Yu. Zanevsky
clean room input gate
climate control
Project status:
basic R&D finished,
(cont. alternative RO Ch.);
assembly workshop
(clean room) close to completion (Sept., 2016)
gas system: delivery to JINR in I 2017
RoC chambers preparation

## Slide 47
TPC assembly tools, cooling & laser calibration system:
outer thermal
screen
front thermal
screen
ready for production
TPC deformation:
max = 32 µm

## Slide 48
triple-stack MRPC
active area of TOF barrel ~56 m2
number of channels 13 824
TOF Barrel
The barrel consist of 12 super-modules (two modules connected together)
readout board with strips
Project status:
- 90% readiness for the mass production
Leader: V. Golovatyuk

## Slide 49
beam test results
Time resolution in dependence of rotation in surface YZ
Efficiency and time resolution of the MRPC versus HV
Time resolution in dependence from the position along strip

## Slide 50
ARTMASH (Minsk, Belarus)
MRPC
TOF Barrel: mass production preparation status
module housing was developed in close cooperation with NC PHEP BSU
and “ Artmash” (Minsk, Belarus)
Workshop for the TOF mass-production
basic elements - NINO & HPTDC chips have been purchased
sufficient to produce read-out
electronics for the TOF +
reserve (~24000 channels).
Notes: The TOF module housing was developed in close collaboration with NC PHEP BSU and “Artmash” (Minsk, Belarus). It consists of two volumes: the volume for detectors filled with the gas mixture and the volume for electronics and cables. One prototype of the module housing is available now. Total 28 boxes planned to produce to the end of the year.

## Slide 51
Fast Forward Detector (FFD)
JINR + Radium Institute (St.Petersburg).
Provides:
T0 for TOF, beam adjustment & collision L0-trigger
Fig. 3
the achieved time resolution fits the requirement
FFD prototype module
Status:
procurement of necessary elements;
production in accordance with the schedule.
Leader: V. Yurevich

## Slide 52
L ~35 cm (~ 14 X0), Pb+Scint. (4x4 cm2) read-out: WLS fibers + MAPD
integration with the MPD - design is completed
Leaders: I. Tyapkin, A. Ol‘shevsky
TDR - in preparation
Ecal (shashlyk type):
performance fits the requirements
the time scale without redundancy
- participation in the MPD experiment;
- mass production of Ecal modules in China;
- production first 10 test modules
Agreement between JINR and Tsinghua University has been signed on:

## Slide 53
FHCAL: for determination of reaction plane and centrality
2-arm (left/right) calorimeter (at ~3.2 m from the IP)
each arm consists of 45 modules.
Ein
Eout
module preproduction:
agreement on production of 9 mod. is signed;
agreement on production of the rest 81 mod.
for the whole FHCal is in preparation;
scintillator tiles are under production at Vladimir plant;
lead absorber & mechanics are ready for assembling;
first 9 FHCAL modules are under construction now.
Leader: A. Ivashkin
Institute for Nuclear Research RAS
Transverse granularity allows to measure:
the reaction plane with the accuracy ~ 200-300
the centrality with accuracy below 10%.
In cooperation with MEPhI

## Slide 54: CBM-MPD consortium for R&D and production of IT modules manifests efficient cooperation since 2008
IT: workshop for microstrip detector assembly & test
the clean room workshop
has started operation in 2015.
CERN & JINR have signed MoU for manufacturing the STS carbon fiber space frames for NICA (BM@N & MPD) and FAIR
D. Gross in the workshop
- put in operation
the first test stand for the in-beam tests of the assembled boards with silicon sensors
– put in operation
the Probe-station automat for DSSD QA

## Slide 55: BM@N ST comprises four first stations of CBM STS
CBM STS: 8 stations
BM@N ST: 4 stations
ladder
1220 sensors:
6.2 × 6.2 cm2
module
252 single /
324 daisy-pairs
900 / 220
260 / 216
60 / 60
+ a number of “half” sensors
Double-sided-double-metalized sensors from Hamamatsu
and CiS
(pitch 58 um, stereo angle 7,5 degrees)
sensor: 0.3% X0
r/o cables: 2×0.11% X0
6.2 × 4.2 cm2
6.2 × 2.2 cm2
3.2 × 2.2 cm2

## Slide 56
NICA program
in spin physics
SPD project preparation stage

## Slide 57
Study of nucleon spin structure
Matveev-Muradyan-Tavkhelidze-Drell-Yan mechanism and SIDIS processes – are good tools for these measurements
Direct photons production
(gluon polarization)
the sum rule:
It will allow to measure all 8 intrinsic-transverse-momentum dependent PDFs (at leading twist) in one experiment
must confirm
NICA collider will provide collisions of protons and deuterons with
all combinations of polarization – transversal and longitudinal
Notes: Study of nucleon spin structure must prove the sum rule and to solve a puzzle of “spin deficit”. NICA collider will provide collisions of protons and deuterons with all combinations of polarization – transversal and longitudinal. It will allow to measure all 8 intrinsic-transverse-momentum PDFs at leading twists in one experiment. MMTDY mechanism and SIDIS processes are good tools for these measurements.

## Slide 58
experiment | CERN, COMPASS-II | FAIR, PANDA | FNAL, E-906 | RHIC, STAR | RHIC-PHENIX | NICA, SPD
mode | F.T. | F.T. | F.T. | collider | collider | collider
Beam/target | π- , p | anti-p, p | π- , p | pp | pp | pp, pd,dd
Polarization:b/t | 0; 0.8 | 0; 0 | 0; 0 | 0.5 | 0.5 | 0.7
Luminosity | 2·1033 | 2·1032 | 3.5·1035 | 5·1032 | 5·1032 | 1032
√s , GeV | 14 | 6 | 16 | 200, 500 | 200, 500 | 10 - 26
x1(beam) range | 0.1-0.9 | 0.1-0.6 | 0.1-0.5 | 0.03-1.0 | 0.03-1.0 | 0.1-0.8
qT, GeV | 0.5 -4.0 | 0.5 -1.5 | 0.5 -3.0 | 1.0 -10.0 | 1.0 -10.0 | 0.5 -6.0
Lepton pairs, | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+, e+e-
Data taking | 2015 | >2025 | 2013 | >2016 | >2016 | >2020
Transversity | NO | NO | NO | YES | YES | YES
Boer-Mulders | YES | YES | YES | YES | YES | YES
Sivers | YES | YES | YES | YES | YES | YES
Pretzelosity | NO | NO | NO | NO | YES | YES
Worm Gear | NO | NO | NO | NO | NO | YES
Direct γ | NO | NO | NO | YES | YES | YES
Experiments studying nucleon spin structure

## Slide 59
SPD/NICA will provide unique opportunity
not available at other facilities
to study all of the PDF in one experiment
and obtain the comprehensive information
on the nucleon spin structure
at high statistical level
with min. systematic uncertainties

## Slide 60
some events
Ione source

## Slide 61
Laboratory hosted
the 15-th international conference SQM in July 2015

## Slide 62
Physics targets for the exploration of first order phase transitions in the region of the QCD phase diagram accessible to NICA & CBM and possible observable effects of a “mixed phase culminates this year in the release of the “NICA White Paper” as a Topical Issue of the EPJ A (July 2016).
111 contributions,
188 authors
from 24 countries
New issues: NICA White Paper, SQM proceedings

## Slide 63
In the medium-term prospect the NICA complex will be
the only facility in Europe providing unique high intensity ion beams
(from p to Au, p and d)
in the energy range from 2 – 27 GeV (c.m.s.),
which could be used for both fundamental and applied researches.
Researches at the NICA complex will contribute to
discovery and study of new forms of nuclear matter;
comprehensive study of nucleon spin structure;
applied researches, like irradiation of biological objects
by heavy ion beams (space mission program) etc.
“It is clear that both FAIR and NICA could have an advantage in developing and extending explicitely their collaboration….”

## Slide 64
Main Research Infrastructure in Particle and Nuclear Physics
NICA – Complementary Project
New issue of the ESFRI Roadmap

## Slide 65
RF Governmental disposal

## Slide 66
Agreement
between
the RF Government
and
the Joint Institute for
Nuclear Research
has been signed

## Slide 67
Concluding remarks
The construction of accelerator complex
and both detectors BM@N & MPD
is going close to the schedule
Physics program development is in progress,
it indicates competitiveness with other experiments
RF Governmental disposal is
an important contribution to the NICA project
The cooperation on all NICA parts is growing
New partners are welcome to join NICA

## Slide 68
Thank you!
NICA
FAIR
CERN
the cooperation makes us stronger!