## Slide 1: Trends in integrated circuit design for particle physics experiments
Eduard ATKIN
dep. of Electronics & ASIC Lab
e-mail: evatkin@mephi.ru
tel. +7(499) 324-25-97
2nd International Conference on Particle Physics and Astrophysics (ICPPA-2016) 10-14 Oct 2016 , Moscow

## Slide 2
Application Specific Integrated Circuits (ASICs) are one of the key complex technologies available to designers of multichannel detectors
A whole number of factors makes ASICs essential to Particle Physics and Astrophysics experiments. Among them the most important ones are: integration scale, low power dissipation, radiation tolerance
In order to make possible future experiments in the intensity, cosmic, and energy frontiers today ASICs should provide new level of functionality at a new set of constraints and trade-offs, like low-noise high-dynamic range amplification and pulse shaping, high-speed waveform sampling, low power digitization, fast digital data processing, serialization and data transmission
Outline

## Slide 3
All integrated circuits, necessary for physical instrumentation, should be radiation tolerant at new, earlier not reached, level (hundreds of Mrad) of total ionizing dose and allow minute almost 3D assemblies
The presention is based on literary source analysis and presents overview of the state of the art and trends in nowadays chip design, basing partially own ASIC lab experience. That shows a next stage of micro- and nanoelectronics usage at physical instrumentation
Outline (2)

## Slide 4
to present:
Trends in integrated circuit design: history, state-of-the-art & what`s next
Tools and typical design routes, finishing in chip prototyping
Example projects of ASICs
Conclusions
Aim

## Slide 5
Moore Era

## Slide 6
Up-to-date world-wide technologies

## Slide 7: Wafer leaders

## Slide 8: Moore law continuation

## Slide 9: Still Science-Fiction – Gate-All-Around Transistor

## Slide 11
Technology variety
K.Roy, B.Jung, A.Raghunathan, Integrated systems in the more-than-Moore Era: Designing low-cost energy efficient systems using heterogeneous components/ 23rd International Conference on VLSI Design, 2010

## Slide 12: More than Moore
International technology roadmap for semiconductors , 2012 Update Overview

## Slide 13
CMS ~1 000 000 custom chips ( of 20 types)
Compact Muon Solenoid
Notes: How many people?

## Slide 14: How could future systems in detector instrumentation look like?
Ideally based on hybrid technologies (at element, chip, package, board and finally system levels)
Highly integrated very sensitive analog front-end
Digitization at earliest stage
Signal processing mostly in digital domain (DSP)
High data rates via output interfaces with speed in multi-Gb/s range
Big data processing (for ex. CMS detector raw data >1000 Pbyte/day (1 Mbyte x 40 MHz))
They will not be cheaper than today

## Slide 15
The increasing quantity of elements at a simultaneous increase in their complexity and density. Moore law is still valid  Increase in integration scale
Digital signal processing part more and more replaces analog one. (250nm  10 Kgates/mm2 … 28 nm  3900 Kgates/mm2)
Design cost increase comparing to the one of manufacture
Design timeline and number of prototype cycles (respins) are reduced
For the majority of projects the minimum set of ASICs is to be developed in a one well verified technology (LHC  IBM 130 nm, SLHC  TSMC 130&65 nm, FAIR  UMC 0.18 µm)  Standardization
ASIC development trends

## Slide 16
ASIC adaptation for other projects as criterion of economic efficiency  Universalization
Functionality increase at a limited power consumption budget
Increase in demand for a high technology (expensive) product. The accent at design is done at system (architectural) questions  SOCs (systems on a chip) dictate a mixed-signal character of design route
The demanded number of ASIC wafers is small and can't interest a manufacturer (106 channels at ~100 chs/chip and ~1000 chips/wafer ~10 wafers only)
ASIC development trends (2)

## Slide 17
Design is based on the usage of constantly modernized:
Computer Aided Design (CAD) systems (Cadence, Mentor Graphics, Synopsys, Agilent),
technological libraries or Design Kits (elements, standard digital and IP blocks), including
design rules of manufacturer, the quantity of which quickly grows for advanced technologies (> 2000 for 22 nm)
Necessity of a fast and actually continuous retraining of experts
Close integration of the design centers for both chip and system (hardware) level
ASIC development trends (3)

## Slide 18
Use technologies more and more advanced (with life time behind 2020), but well characterized for design tools and having a reasonable cost  UMC ММRF CMOS 0.18 µm – main technology for FAIR (choice of 2004)
Extremely compressed timeline for each cycle of custom design (4-6 months) and the presence of the necessary updated CAD tools at all levels of design
Skilled staff of young engineers (till 2020-2023 at least)
Start-to-finish (system level) design is necessary: Structural and behavioral modeling  Design of IP blocks at transistor level and that of systems at high-level language  Layout  Verification (ERC, DRC, LVS, PE, PS)  GDSII
Technology choice for FAIR

## Slide 19
Improvement of radiation hardness against total dose effects for new commercial CMOS processes. At the same time there is a wide spread of parameters among various manufacturers and no guarantee of long-term stability
Radiation-hardness processes lag behind commercial ones for 5-7 years (more than three generations according to Moore)
Radiation hardening of modern ASICs is provided by a wider usage of commercial CMOS processes and a refinement of different methods and means, used at early design stages (rad-hard by design)
Trends for radiation-hardened ICs
R. Lacoe, Improving Integrated Circuit Performance Through the Application of Hardness-by-Design Methodology IEEE Transaction on Nuclear science, v. 55, N4, 2008, p.1903-1925

## Slide 20
Rad-hard technologies are not economically efficient. For them there exists only a small volume of orders
Designer experience allows to carry out only a correct choice of the manufacturer, who can provide specific target requirements
Active investigation of radiation effects for new bulk CMOS technologies and their compiling into the standard of design rules and CAD tools (Calibre, Assura, PVS, etc.) both at element and behavioral levels
Trends for rad-hardened ICs (2)

## Slide 21
A number of rad-hard applications will demand the design of rad-hard components and their manufacture in a radiation hardened technology to meet rigid requirements. The part of such ASICs will be decreased each year
Continuous improvement of very complex rad-hard systems will critically depend on the introduction of commercialized microelectronic innovations in these systems
Raising the limiting complexity of these systems to the level, reached in commercial technologies, will demand a shift of many projects in the direction of creating radiation-tolerant components, using traditional commercial technologies, applying the methods of maintaining an acceptable radiation hardness
Short summary on rad-hard ASICs

## Slide 22: Actual task – analytical comparison of technologies by the radiation hardness:
1) Industrial (commercial) CMOS technology with use of methods “rad-hard-by-design”
2) Rad-hardened technology, according to the Moore law, lags more than 3 generations behind the commercial CMOS one
Thus, the practical dilemma is:
What is better
either a rad-hard 350 nm process (for example, silicon-on-isolator)
or
a bulk CMOS 130 (90) nm process?

## Slide 23: Traditional methods for radiation hardening
Circuital (reservation, redundancy, coding, adaptive biasing and & so on)
Layout (guard rings, ring transistors, and so on)
Technological (low volume CMOS, SOI, trench isolation, & so on). The required rad-hardness level is provided by a semiconductor structure choice and use of the special technological processes

## Slide 24: Rad-hard by design concept
Refinement of traditional non- rad hard libraries for CAD
Elaboration of additional design rules, improving rad-hardness at the following 3 levels of design: 1) Transistor level
2) Level of cells, gates and IP blocks
3) System level
Creation of calibrated test structures and expansion of the scaled element libraries
Monitoring and statistical analysis of the ASIC rad-hard stability, provided at manufacture
Rad-hard tests of chips at both passive and active work modes

## Slide 25
offers at a reasonable price:
licensed CADs of world leaders
access to design rules and technological libraries (design kits) for a number of nanometer and submicron (22 nm … 0.8 µm) processes, including SiGe, SOI, А3В5
access to microsystem and MEMS technologies
provides an inexpensive (from 270 Euro/sq.mm) prototyping of ASICs via advanced processes (down to 22 nm CMOS) using the
so called multiproject approach, when the wafer cost is shared among projects of many customers
since 2013 Europractice provides discounted pricing for Russia as well as EU
Where to manufacture chips? Europractice
www.europractice-ic.com

## Slide 26
http://www.europractice-ic.com/documents_wall_calendar.php

## Slide 27
Number of ASIC projects, manufactured via Europractice in 2015 *
* Europractice annual report 2015, http://www.europractice-ic.com/documents_annual_reports.php
http://www.europractice-ic.com/documents_annual_reports.php
Total: 569 ASICs

## Slide 28
Infrastructure of the ASIC lab at MEPhI
distributed interdepartmental 1 Gb/s local Intranet
clusters of network Linux workstations in a number of departments
licensed microelectronics tools for
computer aided design – Cadence,
Mentor Graphics, Synopsys, Agilent
computer classes for core students
technological libraries starting from 22 nm

## Slide 29: Progress in chip prototyping

## Slide 30
Statistics of projects

## Slide 31: ASIC projects (examples)
128-channel prototype ASIC for data-driven read-out of CBM STS
0.18 um CMOS UMC (Taiwan), consumption 2 mW/ch., shaping time 100 ns, structure 12816/ Chip contains preamplifier, shaper (filter), comparators, cross-point switch, peak detectors, 9-bit ADC and so on
Smart sensor readout ASIC (Rosatom)
0.35 µm SiGe BiCMOS AMS (Austria), temperature range -55…+80 С, consumption 3 mW. Chip contains instrumentation amplifier, 14-bit ADC, two 14-bit DAC, references, electronic termometer and so on
32-channel ASIC for “Nucleon” project (Roscosmos)
0.35 µm CMOS AMIS/OnSemi (Belgium), dynamic range 100 pCb, consumption 2 mW/ch., multiplexed (serial) output
IP blocks for system on chip, controlling a new aircraft engine (Ministry of Education and Science)
0.18 um CMOS UMC (Taiwan), consumption 10 mW/ch., 9-bit ADC

## Slide 32: Some details of ASIC projects
32-channel ASIC for Nucleon project of ROSCOSMOS
128-channel prototype ASIC for СВМ STS

## Slide 33: 1) Threshold voltage shift (~100 mV); 2) Leakage currents --- standard (strip-like) nMOS; --- ring transistors
0.18 µm CMOS of UMC
Tests for total dose effects
(E=8 MeV; F=1011 e/cm2 s; D=0.1; 1; 3 Mrad)

## Slide 34
Phase I: Design of analog and mixed-signal ASICs
Phase II: Prototyping and test technique development
Phase III: First tests and prototype characterization
Phase IV: Qualification of ASICs
Phase V: Preparation for a batch production and testing automation
5 design phases for ASIC development

## Slide 35
Feature: the possibility to perform a mixed-signal simulation for analysis of blocks interaction appears only after the all separate blocks being ready
1. Route «bottom-to-top» (traditional )

## Slide 36
Feature: the usage of mixed-signal simulations at early stage. Due to system synthesis at structure level, it becomes possible to develop fastly the block descriptions at behavioral level – RTL-Verilog, Verilog-A и Verilog-AMS. The same level of abstraction is available with VHDL
2. Route «top-to-bottom»

## Slide 37
Modern ASICs, as a rule, are mixed-signal chips. They surely include both analog and digital parts
Analog part is designed as a custom block, whereas the digital one is described by VHDL or Verilog and then synthesized as a semicustom block, based on standard digital libraries
Now a system simulation at element (transistor) level requires unacceptably a lot of time
Usage of high description languages and software tools for hierarchy design allows to perform simulation with different abstraction level of blocks
General principles of mixed-signal design

## Slide 38: Traditional design routes

## Slide 39
Customer – Rosatom
Design duration – 8 months of 2010
Chip planning in SoC Encounter (Cadence)
Smart pressure sensor readout ASIC

## Slide 40
Name | IA specs
Opamp gain | 96 dB
Unity gain frequency | 2 MHz
Phase margin | 70 degree
Consumption current | 100 µA
RMS noise | 20 nV/Hz1/2
Temperature range | -55…+80 oС
Input current | 5 nA
Offset voltage | 100 µV
Instrumentation amplifier

## Slide 41
Prototyped via Europractice in 2010: SiGe 0.35 µm BiCMOS of AMS
Smart sensor ASIC layout

## Slide 42
Test bench: circuit and board

## Slide 43
14-bit DAC
Name | DAC1
Number of bits | 14 bits
Output range | 3,9 V
Differential nonlinearity | 1 LSB
Integral nonlinearity | 2 LSB
Consumption current | 80 µA

## Slide 44
CSA
Opamp
Comparators
PD
T/H
S/H
Cross-point
switch
Driver
Shaper
Arbitration
Logic
MUX
Control
Logic
IP blocks
ADC
Analog readout
chain
Derandomizer
HDR
readout
Data-driven
readout
Slow
Control
Tasks:
Track finding
Calorimetry
Charge detection
Time of flight
How to build an hierarchy?
Library of reusable IP blocks
Parameters:
Consumption
Speed
Dynamic range

## Slide 45
1. International technology roadmap for semiconductors , 2009 Executive summary http://www.itrs.net/Links/2009ITRS/2009Chapters_2009Tables/2009_ExecSum.pdf
2. H. Spieler, Electronics and Signal Processing //XI ICFA School on Instrumentation in Particle Physics, Bariloche, Argentina , 2010 www-physics.lbl.gov/~spieler
3. A.Marchioro, Past and Future of Microelectronics in HEP // TWEPP-2015
4. Europractice annual report 2015. www.europractice-ic.com/docs/Annual_report_2015.pdf
R. Lacoe, Improving Integrated Circuit Performance Through the Application of Hardness-by-Design Methodology IEEE Transaction on Nuclear science, v. 55, N4, 2008, p.1903-1925
7. K.Roy, B.Jung, A.Raghunathan, Integrated systems in the more-than-Moore Era: Designing lowcost energy efficient systems using heterogeneous components/ 23rd International Conference on VLSI Design, 2010
8. M. Weber Highlights and Trends of Detector Instrumentation and Technology Development in Germany // TWEPP-2016
9. A. Klotz, Cadence EMEA, Science-Fiction becoming Reality 2016, MIET
10. http://www.semiwiki.com
References

## Slide 46
Conclusions
The future of instrumentation is tightly bound with a wide usage of ASICs due to the new challenge in integration scale
Commercial technologies available today are well ahead of most requirements foreseen for particle physics` ASICs
The solution of system (architectural, structural) problems will demand substantially higher efforts to create not separate components, but whole systems on chip (SoC)
Almost all new chips have a mixed-signal character
Nowadays the design is based on microelectronic CADs and the adapted Design Kits of the chosen manufacturer
Reduction of timelines for design, extension of reusable IP block libraries, new level of system tests for readout electronics – all of that requires the usage of advanced CAD in distributed fast networks of powerful computing clusters

## Slide 47
Conclusions (2)
The “Rad-hard by design” approach for commercial CMOS technology is considered to be the best way of providing an acceptable rad-hardness by circuital and layout techniques.
For rad-hardness and temperature stability of the chips it is important to refine the existing libraries and design routes
Long term planning becomes an extremely important factor, especially taking into account the “life time” of both the chosen technology and the design staff
The necessity of much stronger collaboration and coordination between all participants, sharing: the process of preparing human resources; the cost of expensive CAD and chip prototyping as well as updating existing design competences

## Slide 48
Спасибо за внимание

## Slide 49: Backups

## Slide 50
THE FEDERAL TARGET PROGRAM "DEVELOPMENT OF ELECTRONIC COMPONENT BASIS AND RADIOELECTRONICS"
Approved by the Government on November, 26th, 2007, decree N 809
2 main target indicators:
– The technological level of modern electronic component basis is estimated, basing on the one of microelectronic products, mastered in manufacture
    2008  0.18 µm
            2011  0.09 µm
                2015  0.045 µm
– There should be created 64 chip design centers in Russia
Important current tasks for Russia:
A new Federal program on developing a chip design center network, comprising up to 150 centers, has been approved
Creation of an advanced national photomask center
Technological level in Russia

## Slide 51
Number of ASIC projects, manufactured via Europractice by Russian teams*
* Europractice annual report 2015, С.38
www.europractice-ic.com/docs/Annual_report_2015.pdf

## Slide 52: ASIC for Nucleon project*
Большой динамический диапазон (100pC), потребление 2mW/ch, 32 канала
Период проектирования 2005-2009
AMIS 0.35 um CMOS
6 итераций:
Analog, 16 CSAs (включен в отчет Europractice 2005г. ) фев 2005
Mixed-signal, 4+2(тест.) CSA+SH+T&H+MUX+Driver сент. 2006
Mixed-signal, 4+2(тест.)CSA+SH+T&H+MUX+Driver фев. 2007
Mixed-signal, 32+2 (тест.) CSA+SH+T&H+MUX+Driver апр. 2007
Mixed-signal, 32+2 (тест.) (включен в отчет Europractice 2009г.) CSA+SH+T&H+MUX+Driver сент. 2009
Мелкосерийное производство. Mixed-signal, 32+2 (тест.) CSA+SH+T&H+MUX+Driver апр. 2012
Late 2014 ASIC has been launched from Baikonur to the Space
* ROSCOSMOS project

## Slide 53: ASIC Structure

## Slide 54: От 4 (+2) к 32 (+2) каналам
Differential Current drivers
Digital part
References
34 chs
6 chs

## Slide 55: Scope diagrams
CSA structure
Output current driver
CSA/shaper response
Typical waveforms
CSA tail adjustment