## Slide 1: Computer modeling of PMT Hamamatsu R11410-20
Dmitry Akimov, Ekaterina Kozlova
NRNU MEPhI
ICPPA-2016, 10-14 October 2016, Moscow

## Slide 2: Emission two-phase detectors for rare processes
RED-100 inner construction
Electroluminescence signal is very intensive (about two orders higher than scintillation signal) ->coming to edge of linear PMT work

## Slide 3: PMT’s principle of work
It is possible to describe reproduction on the i-th dynode with secondary emission coefficient δ and electron collection efficiency coefficient n:
where k and α are coefficients depending dynode’s behavior.
Based on this, it is possible to represent gain for each dynode:
Accordingly, total gain is:
Or the overall gain can be expressed in terms of the high-voltage supply:
where V is supply voltage, εi is a fraction of the supply voltage VB owed to the action of the voltage divider circuit.

## Slide 4: PMT’s principle of work
For each dynode ε is:
Ri is resistance of i-th circuit part and R is total resistance.
Voltage divider circuit for R11410-20
PMT R11410-20

## Slide 5: PMT’s principle of work. Gain dependence on supply voltage
Sample gain dependences on voltage for some Hamamatsu models
Deviation from power law at high anode currents
Dependence on voltage:

## Slide 6: Coefficients calculation at formula
From experimental data for PMT №KB0278:
For Hamamatsu typical gain:
Solution is:
Chart: Voltage, V
| 1450 | 1550 | 1600 | 1650 | 1750
real gain | 25124843.9451 | 55555555.5556 | 79119850.1873 | 109862671.6604 | 200842696.6292

## Slide 7: First divider models
For current reconstruction between i-th and i+1-th dynodes arbitrary behavioral dependent source was used and current can be set according to formula:
Simplified scheme
right
wrong

## Slide 8: First divider models
Dynode current is:
Anode current is:
That model is also wrong because potential is changing incorrectly during work.
right
wrong

## Slide 9: Problems and solutions
And problem in PMT modeling was found – because of voltage source has zero resistance, current from last dynodes flows through it to earth and don’t come to divider circuit. It leads to incorrect potential between dynodes and accordingly to incorrect total gain.
And there are solution – let’s change voltage source to current voltage-controlled source! Current source has infinite resistance!

## Slide 10: Final model
Divider current is determined instead of voltage source by current source which is controlled by potential difference between last dynode and anode:

## Slide 11: Modeling results, G=f(V)
Gain dependence on supply voltage. Model(1) and experimental (2) characteristics for PMT№ KB0278
Gain dependence on supply voltage. Model(1) and typical gain(2) characteristics for Hamamatsu R11410-20
Chart: Voltage, V
| 1450 | 1550 | 1600 | 1650 | 1750
model gain | 27604000 | 55856500 | 78067000 | 108044600 | 201147000
real gain | 25124843.9451 | 55555555.5556 | 79119850.1873 | 109862671.6604 | 200842696.6292
Gain
Voltage, V

## Slide 12: Modeling results, G/G0=f(Ia)
Gain dependence on anode current for PMT № КВ0278: 1 - experimental, 2, 3, 4, 5 – modeling for Ri = 1,5, 1,1, 1 и 0,5 MOhm
Chart: Anode current, μA
| 1.4840000000000001E-2 | 7.3999999999999996E-2 | 0.14900000000000024 | 0.29800000000000032 | 0.75300000000000189 | 1.526 | 2.3159999999999967 | 3.1319999999999997 | 3.9849999999999999 | 4.8599999999999985 | 6.6959999999999864 | 8.69 | 10.848000000000001 | 13.188000000000001 | 15.743999999999998 | 18.648 | 21.88 | 30.071999999999999 | 38.612000000000002 | 41.376000000000005 | 42.552 | 43.36 | 44.949999999999996 | 45.42
real | 1 | 0.9973 | 1.004 | 1.004 | 1.0148 | 1.0283 | 1.0404 | 1.0553 | 1.0741 | 1.0916 | 1.128 | 1.1712 | 1.2183 | 1.2695 | 1.3261 | 1.3962 | 1.4744 | 1.6887 | 1.8585 | 1.7426 | 1.593 | 1.4609 | 1.2116 | 1.0202
model | 1 | 1 | 1.0006 | 1.017 | 1.0349 | 1.0743 | 1.2216 | 1.3652 | 1.7361 | 1.7749 | 1.8155 | 1.8267
1 MOhm | 1 | 1.0358 | 1.0666 | 1.2043 | 1.3328 | 1.6566 | 1.744 | 1.8271
0.5MOhm | 1 | 1.003 | 1.0197 | 1.1045 | 1.2502 | 1.471 | 1.6059 | 1.6885 | 1.7837 | 1.8482
1,5MOhm | 1 | 0.9985 | 1.0517 | 1.3819 | 1.7507 | 1.8409

## Slide 13: Modeling results, G/G0=f(Ia)
Experimental (1) and model (2) gain dependences (for R = 1.1 MOhm) on anode current for PMT № КВ0278 enlarged
Chart: Anode current, μA
| 1.4840000000000001E-2 | 7.3999999999999996E-2 | 0.14900000000000024 | 0.29800000000000032 | 0.75300000000000189 | 1.526 | 2.3159999999999967 | 3.1319999999999997 | 3.9849999999999999 | 4.8599999999999985
real | 1 | 0.9973 | 1.004 | 1.004 | 1.0148 | 1.0283 | 1.0404 | 1.0553 | 1.0741 | 1.0916
model | 1 | 1 | 1.0006 | 1.017 | 1.0349

## Slide 14: Conclusion
A SPICE model for the simulation of the divider behavior of a PMT has been constructed. Model parameters were extracted from experimental and typical Hamamatsu gain. Problem with incorrect potential behavior was found and solved (as we know, first time in the world). The results of simulation are in a reasonable agreement with the experimentally measured characteristics of the PMT with serial # KB0278. The model can be used for simulation of any type of PMT.

## Slide 15: Thank you for attention!