## Slide 1: DSSD based detection system of the DGFRS-2 setup: design, results, developments Yu.S.Tsyganov1, D.Ibadullaev1,2, A.N.Polyakov1, A.A.Voinov1, M.V.Shumeiko1 1-JINR(Dubna), 2-INP(Almaaty)1
Introduction:
Synthesis of SHE at the Dubna Gas-Filled Recoil Separator , ICPPA-2022 (SUMMARY)
New gas-filled separator (DGFRS-2), it’s DSSD based detection system : present status
Applications in long-term experiments with DC-280 HI beams; .., two last years new experiments: 48Ca+232Th, 238U+40Ar, 242Pu+50Ti (preliminary), 242Pu+54Cr , ..some problems
SUMMARY
SUMMARY p. 3) from me ICPPA 2022
3) System is ready for nearest future experiments
with 48Ca, 50Ti,54Cr projectile. ICPPA 2024..
ICPPA 2024,
October 22-25
Field of interest:
Nucl. Phys. heavy ion-> synthesis/properties SHE
detection system  Real -Time algorithm of background
signals suppression
Z=114-118
The Dubna Gas-Filled Recoil Separator,
FLNR(JINR)

## Slide 2: The DGFRS-2 setup…
Cyclotron ~ 1 pµA…10 (48Ca beam, 50Ti,58Fe, 54Cr in a nearest future >5 pµA)
Actinide target (rotating) to apply high intensity for a long time
differential pumping system
Gas –Filled Separator ( to suppress primary beam and other backgrounds )
Detection system ( DSSD+ΔE(gaseous)+electronics + software(Builder C++) )
DGFRS-2
new Dubna Gas-Filled Recoil Separator
(since 2020)
1994-2017
24-cm target,
12 sectors
/present status/
DGFRS-1
DGFRS-2
Yu.Ts.Oganessian et al. NIM A 1033(2022) 0166640
Manufacturing of higher diameter
(48 cm) rotating target is in progress now..

## Slide 3: ΔE low pressure pentane-filled DGFRS#2 detector
Alpha 5.4
~8.2 ch
Z=114
EVR
background
240 m x 60 mm
242Pu+48Ca287Fl+3n (~2..4 pµA)
`
Vc=-100, Va=+310 , VADD =-200 V
Cathode 20µ-1mm…
W(Au) wire @ expense ~1L/month liquid
D(a-c)~ 6 mm; ha =2 mm; hc=1mm
W(a)=20 µ; W(c) =10 µ.
170Er+50Ti
Calibration reaction
Digi 14.5 keV
Front strip
~ 45 keV FWHM
~ 33 keV FWHM
Back strip #2

## Slide 4: NEW DSSD from Micron Scd. ( since September 2024) strips: 48 /front, 96/ back, 80 /side

## Slide 5
Block-diagram of THE DGFRS#2 two branch spectrometer
One horizontal and one vertical strip channels are shown (+ one ΔE)

## Slide 6
48Ca  50Ti  54Cr
242Pu + 50Ti 292Lv*
238U + 54Cr 292Lv*
2022 to 2024 experiments:
} Cross section?
// instrumentation
tests too…
imperative

## Slide 7: View of Control system #1

## Slide 8
PC simulation
EVR , Z=116
First event of Lv EVR registered energy
238U+54Cr Lv*
D.Ibadullayev, Yu.Tsyganow et al.
TechRxiv.20108918.v1, IEEE, 2022
,2023

## Slide 9
May-june 2024 experiment
3n+4n
+1 October 2024,
..preliminary

## Slide 10: Problems, questions…
1) Rotating target D/24 cm now, j~2 -2.5 pµA both for 50Ti and 54Cr projectiles from DC-280. This design for 48Ca ~ one week up to 7 pµA
Status: in progress now D/48 cm manufacturing and tests (DGFRS-3)
2) non stable ΔE chamber operation under rate greater ~4-6E+03 s-1, drop of efficiency etc…
Status: solved by using additional
negatively biased plane (~ -200 Volts)
3) Radiation DSSD instability. (see below.., as far as I can see –main problem)

## Slide 11: On the DSSD radiation damages (three DSSD since ~2020)
Detector #1
Detector #2

## Slide 12
Reaction 242Pu+50Ti Lv* May 22.. June 24 / 2024 + September 09 -October 28/2024
Detector #3
It was before std=14.1 keV
Strip back #2
Beam was switch off
September 09 -October 28/2024
Detector #4

## Slide 13
Summary
The DGFRS-2 Detection system has been designed and successfully applied in long term HI experiments
Reactions: new superheavy isotopes were discovered, new decay modes:
243Am + 48Ca , 286Mc, 264Lr, α-decay of 268Db, SF 279Rg,
232Th + 48Ca , 268Sg, 272Hs, 276Ds, 275Ds
238U + 54Cr , 288Lv
242Pu + 50Ti , 289Lv, 280Cn
// problems with DSSD radiation stability & ΔE gaseous detector at J >~ 3..5 pμA from DC-280 cyclotron/
With ΔE ~ solved with applying additional negative ~ -200..220 V electrode
There are problems with DSSD at J ~108 ions/ cm2 (in progress now )(~ there are trivial solutions.. not good, as far as I can see)
Nearest future general conclusions (as a reasonable scenario for Z=119 synthesis)
54Cr ~ closed ;  50Ti = open.

## Slide 14
DGFRS-2 team
Thank you for YOUR attention!

## Slide 15
48Ca 50Ti 54Cr
245Cm + 48Ca 293Lv*
242Pu + 50Ti 292Lv*
238U + 54Cr 292Lv*
Synthesis of the same nucleus in different reaction
Decrease of cross section in transition from 48Ca to
50Ti ~10
54Cr ~(+)150
Help #1
From presentation by N.Kovrizhnykh 01 July

## Slide 16
Synthesis of new element 119
243Am(54Cr,3-4n)293,294119 249Bk(50Ti,3-4n)295,296119
Perspectives
237Np(48Ca,3-4n)281,282Nh
Identification by correlation method
Help #2

## Slide 17
Help#3