## Slide 1: Muonography on Kamenny Island in Lake Kubenskoye

## Slide 2
Research team:
A. Alexandrov, P. Babaev, A. Gippius, S. Gorbunov, V. Grachev, N. Konovalova, Y. Krasilnikova, A. Larionov, A. Managadze, I. Melnichenko, N. Okateva, S. Paramonov, A. Petrukhin, N. Polukhina, T. Roganova, Z. Sadykov, N. Starkov, E. Starkova, D. Strekalina, V. Tyukov, M. Chernyavskiy, V. Shevchenko, T. Shchedrina, D. Zainutdinov, A. Volkov, D.Vozdvizhenskii
2

## Slide 3
Outline
3
4 DETECTOR EXPOSURE
6 DATA PROCESSING AND ANALYSIS
8 FINDINGS
2 MAIN STEPS IN THE EXPERIMENT
7 VERIFICATION
1 OBJECT OF STUDY
3 DETECTOR ASSEMBLY
5 GEODETIC SURVEY

## Slide 4
Object of study
4
Spaso-Kamenny Preobrazhensky Monastery in Lake Kubenskoye (Vologda Region)
Founded in 1260
The Preobrazhenskii Cathedral may contain the crypt of Metropolitan Varlaam, who died in 1533
In 1937, it was blown up
The Preobrazhenskii Cathedral

## Slide 5
Main steps in the experiment
5
STEP 1
Preliminary resource estimation for the experiment
STEP 3
Detector assembly
STEP 5
Detector exposure
STEP 7
Emulsion scanning
STEP 6
Deinstallation of detectors and emulsion development
STEP 2
Production of emulsion by “SLAVICH” company
STEP 8
Track reconstruction and data analysis
STEP 9
Results
STEP 4
Detector installation and geodetic surveying

## Slide 6
Detector assembly
Each detector contained 6 double-sided emulsion plates 10.0 × 12.5 cm2 in size
6
Marking of emulsion plates
1
Stack of plates in the detector
2
Assembled detector
3

## Slide 7
Detector exposure
Exposure time ⁓ 2 months
Fixing the detectors on the platforms
18 Detectors
7

## Slide 8
Geodetic survey
8
It is necessary to reference the spatial position of the detectors to a uniform coordinate system

## Slide 9
Geodetic survey
9
Detector position and direction
Horizontal positions between detectors
Distances between detectors
Detector coordinates

## Slide 10
Geodetic survey for detector 7
10
Detector position and direction
Detector 7
Forward visibility area of the detector
Detector №7

## Slide 11
Orthophotomap with terrain relief
11
Рисунок 5. Топоплан острова Каменный – а), схема р
m
m
m
The color scale designates the height difference on the ground
The detectors are located 3.5 m below the surface of the island in the vicinity of the ruined cathedral

## Slide 12
MT1
MT1
MT2
MT2
VT
VT
Photoemulsion layers
Plastic
Emulsion 1
BT
Data processing and analysis
Emulsion 2
Emulsion 6
12
From the obtained microtracks (MT), volume tracks (VT) are reconstructed in the detector
Side view of the plate assembly in the detector

## Slide 13
Data processing and analysis
13
We count the number of muons in the direction (𝜃,𝜙) in solid angle element Δ𝜃Δ𝜙 (bin)
The rarefaction is associated with the septic in the direction 𝜙
The rarefaction corresponds to a potential cavity
The maximum of muons corresponds to the rarefaction of the density along the (𝜃,𝜙) direction
Detector №7
φ~255˚
Δφ = 3˚, Δθ = 3˚

## Slide 14
14
Depth 0,5 – 1,0 m
Det6, Det7, Det15, Det17, 6 plates
Data processing and analysis
We use maxima that are stable for more than two bins (, )
To determine the position of the cavities, we consider the intersection of maxima from several detectors
Stable maximum from 1 detector
Stable maximum from 2 detectors
Stable maximum from 3 detectors
Stable maximum from 4 detectors
Stable maximum from 5 detectors
Notations:
Depth is measured from the surface of the island in the area of the ruined cathedral (148.5 m above sea level).

## Slide 15
Verification
15
The burial place of A. Piligin
Stable maximum from Det6, Det7
Depth 1,0 – 1,5 m
Registration of visible objects
Size of squares

## Slide 16
16
Depth 1,5 - 2,5 m
Septic
5.0m
Stable maximum from 2 detectors
Stable maximum from 3 detectors
Verification

## Slide 17
Verification
17
Stable maximum from 2 detectors
Det7, Det13
Septic
Depth 1,0 - 2,0 m
Det7, Det10
Det7, Det15

## Slide 18
Findings
18
Depth 0,0 - 1,0 m
The size of the cavity is 0.51.0 m2
It is located at a distance of 1.5 m from the corner
Stable maximum from 3 detectors
Stable maximum from 5 detectors
1.5m
Notes: Now you can see our findings and key results.
First, we found a cavity under the temple wall at a depth of up to 1 m, which has dimensions 0.5×1.0. It is located at a distance of ~1.5 m from the corner

## Slide 19
Findings
19
Stable maximum from 3 detectors
Depth 0,5 - 1,0 m
The size of the cavity is 0.51.0 m2
It is located in the center of the altar

## Slide 20
Findings
20
Stable maximum from 2 detectors
Depth 1,5 - 2,0 m
The cavities under the altar and in the area of the columns
The size of the cavity is .0.0 m2

## Slide 21
Findings
21
Stable maximum from 2 detectors
Stable maximum from 5 detectors
Depth 1,0 - 2,0 m
The size of the cavity is .0 m2
It is brightly visible at a depth of 1.5-2.0 m
7.5 m
Notes: (On this slide you can see a stable maximum from 5 detectors that corresponds to a clearly visible cavity at a depth of 1 to 2 meters. The size of the cavity is ~𝟏.𝟎×𝟐.0 m)
We also found a cavity to the right of the altar at depth of 1 to 2 meters. The size of the cavity is ~𝟏.𝟎×𝟐.0 m

## Slide 22
Findings
22
Stable maximum from 2 detectors
The cavity between the bell tower and the brotherly building
Stable maximum from 3 detectors
Depth 1,0 - 1,5 m
The size of the cavity is .0 m2
The cavity under the stairs

## Slide 23
Results
23
1. The stable registration of A. Piligin's grave, septic tank and well confirm the correctness of the methodology
3. Cavities were discovered between the bell tower and the brotherly building
2. Cavities have been discovered under the destroyed Preobrazhenskii Cathedral

## Slide 24
THANK YOU FOR YOUR ATTENTION !