## Slide 1: Setup for fiber test
F. Dubinin

## Slide 2: Proposal
Power Supply
Power Supply
SiPM
I/O switches
LED
Ampermeter
…
…
x12 channels
…
…
…
…
Fiber under test
Connector
Connector
…
…
I/O switches
x12 channels

## Slide 3: Hot swapping of test sample
50k + 50k resistors limits current by 25μA per SiPM
12 SiPM → 300μA
Power consumption by open SiPM: W = 25V * 25μA = 625μW
FR4 thermal conductivity: 0,3mW/(mm*K) along thickness
Voltage drop during regular operations: 0,1V @ 1μA
- not negligible but reasonable

## Slide 4: LED circuit
Circuit designed to run LED at very beginning of open part of IV curve
Potentiometer allows to adjust LED brightness to get SiPM response of 1 μA
GNL-0603UBC
λ_max = 470nm
S = 1,6 x 0,8 mm2