## Slide 1
A.N. Oleinik1,*, M.O. Berezhnaya1, I.A. Kishchin1,2, A.A. Klenin1, A.A. Podoynitsyn1, I.S. Shablov1,3, P.G. Shapovalov1,4, V.S. Sotnikova1
1 Laboratory of Radiation Physics, Belgorod National Research University, Belgorod, Russia
2 Lebedev Physical Institute, Moscow, Russia
3 Shubnikov Institute of Crystallography of the Kurchatov Research Center, Moscow, Russia
4 National Research Nuclear University ”MEPhI“, Moscow, Russia
*) oleynik_a@bsuedu.ru
Pyroelectric accelerator with quasimonoenergetic electron production: current status and challenges
Report at the 8th International Conference on Particle Physics and Astrophysics (ICPPA-2026)
Moscow, 30th of October, 2026

## Slide 2
Methods for the electrical excitation of materials with spontaneous polarization
Wang, W., Li, J., Liu, H., & Ge, S. (2020). Advancing Versatile Ferroelectric Materials Toward Biomedical Applications. Advanced Science, 8(1), 2003074.
Used materials
Lithium niobate (LiNbO3)
Density: 4.65 g/cm3
Density: 7.46 g/cm3
Pyroelectric coefficient: about 1 × 10-8 C/cm2/К
Pyroelectric coefficient: about 2 × 10-8 C/cm2/К
Dielectric permittivity along polar axis: 43
Dielectric permittivity along polar axis: 44.5
Lithium tantalate (LiTaO3)

## Slide 3
THE SCHEME OF ELECTRON GENERATION IN A PYROELECTRIC ACCELERATOR
Used pyroelectric materials | Temperature change range | Pressure range | Electron flow current | Electron flow energy | Peak X-ray intensity
Lithium tantalate (LiTaO3) Lithium niobate (LiNbO3) | From 10 °C | Up to 100 mTorr (about 15 Pa) | Up to 1 nA | Up to 200 keV | Up to 109 ph/s in 4π
The conceptual design of a pyroelectric accelerator
Scheme for the generation of electrons and photons based on a charge polarity difference on the surface of a pyroelectric material

## Slide 4
THE ELECTRON FLOW IN A PYROELECTRIC ACCELERATOR (1/2)
SELF-FOCUSING
The spot of the self-focused electron flow emitted from a pyroelectric crystal
(R. Ghaderi and F.A. Davani, Appl. Phys. Lett. 105 (2014) 232906.)
The simulation of self-focused electron flow based on a ring-like charge model

## Slide 5
THE ELECTRON FLOW IN A PYROELECTRIC ACCELERATOR (2/2)
LONG-TIME QUASIMONOENERGETIC ELECTRON FLOW
stabilization over a prolonged period, but relatively low energy (up to 100 keV)
a high value of 150–250 keV for a short duration (relative to the cycle duration)
J.D. Brownridge et. al., Appl. Phys. Lett. 78 (2001) 1158.)
S. Mohtashami et. al., JINST 16 (2021) 10017)
The spectrum may contain several quasi-monoenergetic lines that change only slightly over the course of tens of seconds.

## Slide 6
EXPERIMENTAL SETUP IN BELGOROD STATE UNIVERSITY
Standard scheme

## Slide 7
THE INFLUENCE OF TEMPERATURE CHANGE LAW
Stable particle area region
A.N. Oleinik, TPL, 2024, No. 6, pp 3-6 (in Russian)
Real law of changing temperature in the experiment
Rate of temperature shift
Periodic variation of temperature

## Slide 8
STABLE REGIME OF PARTICLE GENERATION IN A PYROELECTRIC ACCELERATOR
Results of testing under two-hour continuous thermal cycling
negative polarity
positive polarity

## Slide 9
STABLE PARTICLE GENERATION AREA IN A PYROELECTRIC ACCELERATOR
UNSTABLE
STABLE
Impact
ionization
influence
Stability diagram of the pyroelectric accelerator in the residual gas pressure–crystal-to-target distance parameter space
Thermal phase-resolved X-ray spectra

## Slide 10
ATYPICAL ELECTRON AVALANCHE IN A PYROELECTRIC ACCELERATOR
I-V curve of observed discharge
I-V curve of Townsend discharge
Massines, F. et. al. Plasm. Phys. Control. Fusion. 47, B577 (2005).
The I-V curves at different pressures of the residual gases
We cannot identify our discharge as a Townsend discharge!
There is no mention of these peaks in the literature.
The electron current peaks coincide with the period of maximum X-ray photon intensity and maximum electron energy.

## Slide 11
Computer simulation of secondary electron motion between target and pyroelectric crystal
А. Oleinik, M.E. Gilts, et.al., Europhysics Letters, (2023) 142 34001
Current (A)
Energy (keV)
Brass
Steel
Titanium
I-V curves at different materials of target
11
ATYPICAL ELECTRON AVALANCHE IN A PYROELECTRIC ACCELERATOR

## Slide 12
CORRELATION BETWEEN AVALANCHE DISCHARGE AND LONG-TERM STABILUTY OF ELECTRON SPECTRUM
long-term monoenergeticity
additional electron wave

## Slide 13
APPLICABILITY FOR CALIBRATION OF PARTICLE DETECTORS
It was performed over 50 thermal cycles at next conditions:
- LiTaO3 single crystal, 20x20x10 (z) mm, cylinder shape;
- Brass target, 50x50x0.4 mm with hole of 0.3 mm diameter;
- Pressure range is 1.5-5 mTorr
- Temperature variation amplitude is 19.3-20.1 °C
- Ortec-CR-012-025-100 surface-barrier particle detector was used to measure electron flux.
°

## Slide 14
COMPUTER MODELING OF ELECTRON FLUX IN A PYROELECTRIC ACCELERATOR
Trajectories of primary electron flux in geometry of an experiment
Dynamic of emittance of electron flux
P.G. Shapovalov et.al., Journal of Instrumentation 19 C09001 2024
The dependence of focal point on radial coordinate of electron emission

## Slide 15
CONCLUSION
There is an area with stable and reproducible electron generation (in space “pressure-distance”) with minimized risk of electric breakdown (at certain temperature variation level)
This area is limited by an influence of impact ionization, the role of secondary electron emission is not so unambiguous
The position of energy peak of electron flux is very sensitive to value of pressure, amplitude of temperature variation, but it is reproducible and can be controllable
Devices based on pyroelectric accelerator concept can be implemented as calibration instruments for different electron detectors with tunable energy peak about several tens of keV

## Slide 16
THANK FOR YOUR ATTENTION!
The research was supported by a grant from the Russian Science Foundation (Project No. 26–72–10002)
A. Oleinik, et. al. J. App. Phys., 132, 204101 (2022).
A.N. Oleinik, et.al., Nuclear Instruments and Methods in Physics Research A 1065 (2024) 169537
P.G. Shapovalov et.al., Journal of Instrumentation 19 C09001 2024
А. Oleinik, M.E. Gilts, et.al., Europhysics Letters, (2023) 142 34001
Karataev, P., Ali, M., Fedorov, K. et al. Quasi-continuous X-ray generation in LiTaO3-based pyroelectric accelerator driven by periodically varying temperature. Sci Rep 15, 31209 (2025).